## Slide 1: Chapter 20
Analysis of MIMO Control Loops
Notes: <<<20.1>>>
### Analysis of MIMO Control Loops ###

## Slide 2: Motivational Examples
All real-world systems comprise multiple interacting variables. For example, one tries to increase the flow of water in a shower by turning on the hot tap, but then the temperature goes up; one wants to spend more time on holiday, but then one needs to spend more time at work to earn more money. A more physical example is provided on the next slide.
Notes: <<<20.2>>>
### Motivational Examples###

## Slide 3: Example 20.1 (Ammonia Plant)
A typical industrial plant aimed at producing ammonia from natural gas is the Kellogg Process.

## Slide 4
In an integrated chemical plant of this type, there will be hundreds (possibly thousands) of variables that interact to some degree. Even if one focuses on one particular process unit - e.g., the ammonia synthesis converters - one still ends up with 5 to 10 highly coupled variables. A typical ammonia-synthesis converter is shown below.

## Slide 5: Figure 20.1: Ammonia-synthesis converter

## Slide 6
The process is exothermic; thus, the temperature rises across each catalyst bed. It is then cooled by mixing from the quench flows. Many measurements will typically be made - e.g., the temperature on either side of each bed.

## Slide 7
The nature of the interactions can be visualized as follows. Say one incrementally opens quench valve 1; then all other flows will be affected, the temperature in zone 1 will drop, this will pass down the converter from bed to bed; as the reaction progressively slows, the heat exchanger will move to a different operating point and finally, the temperature of the feed into the top of the converter will be affected. Thus, in the end, all variables will respond to the change in a single manipulated variable.

## Slide 8
Obviously, these kinds of interaction are complex to understand and, as a result, they make control-system design interesting. Of course, one could attempt to solve the problem by using several SISO control loops, but this might not prove satisfactory. For example, in the ammonia-synthesis plant one could try controlling T1, T3, T5, and T7 by manipulating the four quench valves with individual PID controllers. However, this turns out to be a somewhat nontrivial task, on account of the associated interactions.

## Slide 9: Models for Multivariable Systems
Most of the ideas presented in early parts of the book apply (albeit with some slight enhancements) to multivariable systems. The main difficulty in the MIMO case is that we have to work with matrix, rather than scalar transfer functions. This means that care needs to be taken with such issues as the order in which transfer functions appear. (In general matrices do not commute).
Notes: <<<20.3>>>
### Models for Multivariable Systems###

## Slide 10: State Space Models, Revisited
Linear MIMO systems can be described by using the state space ideas presented in Chapter 17. The only change is the extension of the dimensions of inputs and outputs to vectors.
Notes: <<<20.3.1>>>
### State Space Models, Revisited###

## Slide 11: Transfer-Function Models, Revisited
It is straightforward to convert a state space model to a transfer-function model.
The matrix transfer function G(s) corresponding to a state space model (A, B, C, D) is
Notes: <<<20.3.2>>>
### Transfer-Function Models, Revisited###

## Slide 12
We will use Gik(s) to denote the transfer function from the kth component of U(s) to the ith component of Y(s). Then G(s) can be expressed as

## Slide 13
Definition 20.2: The impulse response matrix of the system, g(t), is the inverse Laplace transform of the transfer-function matrix G(s). For future reference, we express g(t) as

## Slide 14: Matrix Fraction Descriptions
Clearly, all matrix transfer descriptions comprise elements having numerator and denominator polynomials. These matrices of rational functions of polynomials can be factorized in various ways.
Notes: <<<20.3.3>>>
### Matrix Fraction Descriptions###

## Slide 15: Left Matrix Fraction Description (LMFD)
We can write where
This is a special form of Left Matrix Fraction Description (LMFD) for G(s).

## Slide 16: Right Matrix Fraction Description (RMFD)
Let denote the least common multiple of the denominator polynomials in the ith column of G(s). Also, let denote a Hurwitz polynomial of the same degree as Then we can write
where

## Slide 17
This is a special form of Right Matrix Fraction Description.

## Slide 18: Connection Between State Space Models and MFD’s
A RMFD and LMFD can be obtained from a state space description of a given system by designing stabilizing state-variable feedback and an observer, respectively.
Notes: <<<20.3.4>>>
### Connection Between State Space Models and MFD’s###

## Slide 19
Consider the state space model
We assume that the state space model is stabilizable.

## Slide 20
Let u(t) = -Kx(t) + w(t) be stabilizing feedback. The system can then be written as follows, by adding and subtracting BKx(t):

## Slide 21
We can express these equations, in the Laplace-transform domain with zero initial conditions, as
where GN(s) and GD(s) are the following two stable transfer-function matrices:
We see that (GN(s), GD(s)) is a RMFD.

## Slide 22
Similarly, we can use an observer to develop a LMFD. We assume that the state space model is detectable. Consider the following observer
We can express these equations in the Laplace domain as

## Slide 23
We know that, for a stable observer, v(t) 0 exponentially fast, hence, in steady state, we can write
where
Hence is a LMFD for the system.

## Slide 24
The RMFD and LMFD developed above have the following interesting property:

## Slide 25
Lemma 20.1: There always exist a RMFD and a LMFD for a system having the following coprime factorization property:

## Slide 26
Where are defined by

## Slide 27: Poles and Zeros of MIMO Systems
The reader will recall that, in the SISO case, the performance of control systems was markedly dependent on the location of open-loop zeros. Thus, it would seem to be important to extend the notion of zeros to the MIMO case.
Notes: <<<20.3.5>>>
### Poles and Zeros of MIMO Systems###

## Slide 28
We define zeros of a MIMO transfer function as those values of s that make the matrix G(s) lose rank. This means that there exists at least one nonzero constant vector v (zero right direction) such that
and at least one nonzero constant vector w (zero left direction) such that
where s = c is one of the zeros of G(s).

## Slide 29
Note that the number of linearly independent vectors that satisfy depends on the rank loss of G(s) when evaluated at s = c. This number if known as the geometric multiplicity of the zero, and it is equal to the dimension of the null space generated by the columns of G(s).

## Slide 30
System zeros as defined above are not always obvious by looking at the transfer function. This is illustrated in the following example.

## Slide 31: Example 20.3
Consider the matrix transfer function
It is difficult to tell by inspection where its zeros are. However, it turns out there is one zero at s = -3, as can be readily seen by noting that
which clearly has rank 1.

## Slide 32: Example 20.4: Quadruple-tank Apparatus
A very interesting piece of laboratory equipment based on four coupled tanks is shown in the next photo.

## Slide 34: Figure 20.2: Schematic of a quadruple-tank apparatus

## Slide 35
Physical modeling leads to the following (linearized) transfer function linking (u1, u2) with (y1, y2).
Where 1 and (1 - 1) represent the proportion of the flow from pump 1 that goes into tanks 1 and 4, respectively (similarly for 2 and (1 - 2).

## Slide 36
The system has two multivariable zeros that satisfy det(G(s)) = 0:
A simple root-locus argument shows that the system is nonminimum phase for  > 1, i.e. for 0 < 1 + 2 < 1, and minimum phase for  < 1, i.e. for 1 < 1 + 2 < 2.
Also, the zero direction associated with a zero c > 0 satisfies . It then follows that, if 1 is small, the zero is associated mostly with the first output, whilst if 1 is close to 1, then the zero is associated mostly with the second output.

## Slide 37: The Basic MIMO Control Loop
The systems we consider will be square (the input vector has the same number of components as the output vector). Also, all transfer-function matrices under study will be assumed to be nonsingular almost everywhere, which means that these matrices will be singular only at a finite set of zeros.
Notes: <<<20.4>>>
### The Basic MIMO Control Loop###

## Slide 38
We will consider the same basic feedback structure as in the SISO case, i.e., the structure shown on the next slide.

## Slide 39: Figure 20.3: MIMO feedback loop

## Slide 40
The nominal MIMO control loop can be described, as in the SISO case, by certain key transfer functions. In particular, we define
S0(s) : the (matrix) transfer function connecting D0(s) to Y(s)
T0(s) : the (matrix) transfer function connecting R(s) to Y(s)
Su0(s) : the (matrix) transfer function connecting R(s) to U(s)
Si0(s) : the (matrix) transfer function connecting Di(s) to Y(s)

## Slide 42: MIMO Sensitivity Functions
The Sensitivity Functions (used in the expressions on the previous slide) are given by

## Slide 43
Note that, because matrix products, in general, do not commute, special care must be exercised when manipulating the above equations.
Note also that So(s) + To(s) = I and S(s) + T(s) = I. There are also multivariable versions of

## Slide 44: Closed-Loop Stability
We next extend the notions of stability, described in Chapter 15 for the SISO case, to the MIMO case.
Notes: <<<20.5>>>
### Closed-Loop Stability###

## Slide 45
Consider the nominal control loop in Figure 20.3. Then the nominal loop is internally stable if and only if the four sensitivity functions are stable.

## Slide 46: Stability in MFD Form
Stability can also be expressed by using matrix fraction descriptions (MFDs).
Consider RMFD and LMFD descriptions for the plant and the controller:
Notes: <<<20.5.1>>>
### Stability in MFD Form###

## Slide 47
The transfer functions appearing in the sensitivity functions can be rewritten
The above expressions immediately imply the result on the next slide.

## Slide 48: Stability of Feedback Loops Described via MFD’s
Consider a one-d.o.f. MIMO feedback control loop, as shown in Figure 20.3. Let the nominal plant model and the controller be expressed in MFD. Then the nominal loop is internally stable if and only if the closed-loop characteristic matrix Acl(s)
has all its zeros strictly in the LHP, where the zeros are defined to be the zeros of det{Acl(s)}.

## Slide 49: Example 20.5
A diagonal controller C(s) is proposed to control a MIMO plant with nominal model Go(s). If C(s) and Go(s) are given by
is the loop stable?
We need LMFD and RMFD for the plant model and the controller, respectively.

## Slide 50
A simple choice is
and
Then

## Slide 51
All roots of det(Acl(s)) have negative real parts. Thus, the loop is stable.

## Slide 52: Stability via Frequency Responses
The reader may well wonder whether tools from SISO analysis can be applied to test stability for MIMO systems. The answer is, in general, yes, but significant complications arise due to the multivariable nature of the problem. We will illustrate by showing how Nyquist theory might be extended to the MIMO case.
Notes: <<<20.5.2>>>
### Stability via Frequency Responses###

## Slide 53
If we assume that only stable pole-zero cancellations occur in a MIMO feedback loop, then the internal stability of the nominal loop is ensured by demanding that S0(s) be stable.
Consider now the function F0(s), defined as
where i(s), i = 1, 2, …, m, are the eigenvalues of Go(s)C(s). The polar plots of i(j ), i = 1, 2, …, m on the complex plane are known as characteristic loci.

## Slide 54: Stability Result
If the Nyquist contour Cs = Ci  Cr, shown in Figure 5.5 on the next slide, is chosen, then we have the following theorem, which has been adapted from the Nyquist Theorem.

## Slide 55: Figure 5.5

## Slide 56
Theorem 10.1: If a proper open-loop transfer function Go(s)C(s) has P poles in the open RHP, then the closed loop has Z poles in the open RHP if and only if the polar plot that describes the combination of all characteristic loci (along the modified Nyquist path) encircles the point (-1, 0) clockwise N = Z-P times.
Proof: See the book.

## Slide 57: Steady-State Response for Step Inputs
Steady-state responses also share much in common with the SISO case. Here, however, we have vector inputs and outputs. Thus, we will consider step inputs coming from particular directions - i.e., applied to various combinations of inputs in the input vectors. This is achieved by defining
where Kr  m, Kdi  m, and Kd0  m are constant vectors.
Notes: <<<20.6>>>
### Steady-State Response for Step Inputs###

## Slide 58
By using the final-value theorem, we have

## Slide 59
It is also possible to examine the circumstances that lead to zero steady-state errors. By way of illustration, we have the following result for the case of step reference signals.

## Slide 60
Consider a stable MIMO feedback loop, as on the next slide. Assume that the reference R(s) is a vector of the form shown in
The steady-state error in the ith channel, ei(), is zero if the ith row of So(0) is zero. Under these conditions, the ith row of To(0) is the elementary vector ei = [0 … 0 1 0 … 0]T.

## Slide 61: Figure 20.3

## Slide 62: Frequency-Domain Analysis
We found, in the SISO case, that the frequency domain gave valuable insights into the response of a closed loop to various inputs. This is also true in the MIMO case. However, to apply these tools, we need to extend the notion of frequency-domain gain to the multivariable case.
Notes: <<<20.7>>>
### Frequency-Domain Analysis###

## Slide 63: Principal Gains and Principal Directions
Consider a MIMO system with m inputs and m outputs, having an m  m matrix transfer function G(s):
We obtain the corresponding frequency response by setting s = j. This leads to the question: How can one define the gain of a MIMO system in the frequency domain ?
Notes: <<<20.7.1>>>
### Principal Gains and Principal Directions###

## Slide 64
We use vector norms instead of absolute values. Any suitable norm could be used. We will use ||r|| to denote the norm of the vector . For example, we could use the Euclidean norm, defined as follows:
where H denotes conjugate transpose.

## Slide 65: MIMO Gain
A possible way to define the MIMO system gain at frequency  is then to choose a norm for the matrix G that accounts for the maximizing direction associated with the input for U. Thus, we define

## Slide 66
We call ||G|| the induced norm on G corresponding to the vector norm ||U||. For example, when the vector norm is chosen to be the Euclidean norm,
then we have the induced spectral norm for G defined by

## Slide 67
Actually, the above notion of induced norm is closely connected to the notion of singular values. To show this connection, we recall the definition of singular values of an m  l complex matrix . The set of singular values of  is a set of cardinality k = min(l, m) defined by

## Slide 68
We note that the singular values are real positive values, because H and H are Hermitian matrices. We recall that (j) is a Hermitian matrix if H(j) T(-j) = (j). It is customary to order the singular values, as follows:

## Slide 69
We apply these ideas to ||G||. Taking = GHG, we have that

## Slide 70: Tracking
We next consider the frequency-domain conditions necessary to give good tracking of reference signals. We recall that E(s) = So(s)R(s). We can obtain a combined measure of the magnitude of the errors in all channels by considering the Euclidean form of E(j). Hence, consider
Notes: <<<20.7.2>>>
### Tracking###

## Slide 71
We then see that errors are guaranteed small if is small in the frequency band where ||R(j)||2 is significant. Note that So(s) + To(s) = 1, and so

## Slide 72
Using properties of singular values we have
Thus, we see that errors in all channels are guaranteed small if is made as large as possible over the frequency band where ||R(j)||2 is significant.

## Slide 73: Disturbance Compensation
We next consider disturbance rejection. For the sake of illustration, we will consider only the input-disturbance case.
Notes: <<<20.7.3>>>
### Disturbance Compensation###

## Slide 74
For the input-disturbance case, we have
Furthermore, upon application of properties of singular values we have

## Slide 75
We conclude:
Good input-disturbance compensation can be achieved if (Go(j)Co(j) » 1 over the frequency band where
(Go(j)||Di||2 is significant.

## Slide 76: Measurement-Noise Rejection
The effect of measurement noise on MIMO loop performance can also be quantified by using singular values, as shown below. We have, that, for measurement noise,
Thus, good noise rejection is achieved if (To(j) «1 over the frequency band where the noise is significant.
Notes: <<<27.7.4>>>
### Measurement-Noise Rejection###

## Slide 77: Directionality in Sensitivity Analysis
The preceding analysis produced upper and lower bounds that can be used as indicators of loop performance. However, the analysis presented so far has not emphasized one of the most significant features of MIMO systems, namely, directionality.
Notes: <<<20.7.5>>>
### Directionality in Sensitivity Analysis###

## Slide 78: Example
In a MIMO control loop, the complementary sensitivity is given by
The loop has output disturbances given by
Determine the frequency d, the ratio K1/K2, and the phase difference 1 - 2 that maximize the Euclidean norm of the stationary error, ||E||2.

## Slide 79
In steady state, the error is a vector of sine waves with frequency d. We then apply phasor analysis. The phasor representation of the output disturbance is
We see that the error due to output disturbances is the negative of that for a reference signal. Then, we have that, for every ratio K1/K2 such that ||D0|| = 1, the following holds:

## Slide 80
The upper bound on the above slide is reached precisely when the direction of the disturbance phasor coincides with that of the principal direction associated with the maximum singular value of So(jd).

## Slide 81
To investigate the above result for the particular system in this example, we first obtain So(s), by applying the identity To(s) + So(s) = I;
We can now compute the value of  at which (So(j)) is maximal. The singular values of So(j) are shown on the next slide.

## Slide 82: Figure 20.4: Singular values of the sensitivity function

## Slide 83
We see that (So(j)) is maximum at   4.1[rad/s]. Thus, the maximizing disturbance frequency is d = 4.1[rad/s].
The principal directions associated with the two singular values (So(jd)) and (So(jd)) are, respectively given by
We are interested only in u1, which can be expressed as

## Slide 84
Thus, the maximizing solution (i.e., the worst case) happens when

## Slide 85: Directionality in Connection with Pole-Zero Cancellations
Directionality issues also show up in connection with pole-zero cancellations and loss of controllability or observability. Consider, for example, the set-up shown on the next slide.
Notes: <<<20.7.6>>>
### Directionality in Connection with Pole-Zero Cancellations###

## Slide 86: Figure 17.3

## Slide 87
The composite system has realization (A, B, C), where

## Slide 88
We know, from Chapter 3, that pole-zero cancellations play a role in loss of observability or controllability. However, in the MIMO case, directions are also important, as is shown in the following lemma.
Lemma 20.5: The composite system loses observability if and only if  is a pole of system 1 and a zero of system 2 such that there exist an x1 the null space of (I - A1) and C1x1 the null space of C2(I - A2)-1B2.
Proof: See the book.

## Slide 89
Lemma 20.6: The composite system loses controllability if and only if  is a zero of system 1 and a pole of system 2 such that there exist the left null space of (I - A2) and left null space of C1(I - A1)-1B1.
Proof: See the book.

## Slide 90: Example
Consider two systems, S1 and S2 having, respectively, the transfer functions

## Slide 91
We first build a state space representation for the system S1 by using the MATLAB command ss.
It is straightforward (using MATLAB) command eig) to compute the system eigenvalues, which are located at -1 and -3, with eigenvectors w1 and w2 given by

## Slide 92
Also, this system has no zeros.
The system S2 has three poles, located at -1, -2 and -2 and one zero, located at -3. This zero has a left direction and a right direction h, which are given by

## Slide 93
We observe that one pole of S1 coincides with one zero of S2.
S1 output is the input of S2:
To investigate a possible loss of observability, we have to compute C1w2 and compare it with h. We first obtain C1w2 = [-1.414 5.657]T, from which we see that this vector is linearly dependent with h.
Thus, in this connection, there will be an unobservable mode, e-3t.

## Slide 94
S2 output is the input of S1:
To investigate a possible loss of controllability, we have to compute B1 and compare it with . We have that B1 = [-0.707 -0.707]. Thus, this vector is linearly independent of , and hence no loss of controllability occurs in this connection.

## Slide 95: Robustness Issues
Finally, we extend the robustness results for SISO to the MIMO case. As for the SISO case, MIMO models will usually be only approximate descriptions of any real system. Thus, the performance of the nominal control loop can significantly differ from the true or achieved performance. To gain some insight into this problem, we consider linear modeling errors, as we did for SISO systems.
Notes: <<<20.8>>>
### Robustness Issues###

## Slide 96
We will consider two equivalent forms for multiplicative modeling errors (MME):
where G1(s) and Gr(s) are the left and right MME matrices, respectively. We observe that these matrices are related by

## Slide 97
This equivalence allows us to derive expressions by using either one of the descriptions. For simplicity, we will choose the left MME matrix and will examine the two main sensitivities only: the sensitivity and the complementary sensitivity.

## Slide 98
We can then derive expressions for the achievable sensitivities
Note the similarity between the above expressions and those for the SISO case. We can also use these expressions to obtain robustness results.

## Slide 99
Theorem 20.2: Consider a plant with nominal and true transfer function Go(s) and G(s), respectively. Assume that they are related by
Also assume that a controller C(s) achieves nominal internal stability and that Go(s)C(s) and G(s)C(s) have the same number, P, of unstable poles. Then a sufficient condition for stability of the feedback loop obtained by applying the controller to the true plant is
Proof: See the book.

## Slide 100: Example 20.8
A MIMO plant has nominal and true models given by Go(s) and G(s), respectively, where

## Slide 101
We see that G1(s), can be computed from
This yields

## Slide 102
The singular values of G1(s) are computed by using MATLAB commands, leading to the plots shown below.
Figure 20.5: Singular values of MME matrix
We can use the above data to determine what values of T0(s) give guaranteed closed loop stability.

## Slide 103: Summary
In previous chapters, we have considered the problem of controlling a single output by manipulating a single input (SISO).
Many control problems, however, require that multiple outputs be controlled simultaneously; to do so, multiple inputs much be manipulated - usually, subtly orchestrated (MIMO).
  Aircraft autopilot example: speed, altitude, pitch, roll, and yaw angles must be maintained; throttle, several rudders, and flaps are available as control variables.
  Chemical process example: yield and throughput must be regulated; thermal energy, valve actuators, and various utilities are available as control variables.
Notes: <<<20.9>>>
###Summary###

## Slide 104
The key difficulty in achieving the necessary orchestration of inputs is the multivariable interactions, also known as coupling.
From an input-output point of view, two fundamental phenomena arise from coupling - See Figure 20.6.
Figure 20.6: Two phenomena associated with multivariable interactions

## Slide 105
Multivariable interactions in the form, shown in Figure 20.6 add substantial complexity to MIMO control.
Both state space and transfer-function models can be generalized to MIMO models.
The MIMO transfer-function matrix can be obtained from a state space model by G(s) = C(sI - A)-1B + D.
In general, if the model has m inputs, u  m, and 1 outputs, y  , then
  the transfer-function matrix consists of an l  m matrix of SISO transfer functions, and
  for an n-dimensional state vector, x   n, the state space model matrices have dimensions A   nn, B   nm, C   ln, D   lm.

## Slide 106
Some MIMO model properties and analysis results generalize quite straightforwardly from SISO theory:
  similarity transformations among state space realizations
  observability and controllability
  poles
Other MIMO properties are more subtle or complex than their SISO counterparts, usually due to interactions or the fact that matrices do not commute - e.g.,
  zeros
  left and right matrix fractions.