## Slide 1: CONTROL SYSTEM DESIGN
Graham C. Goodwin
Stefan F. Graebe
Mario E. Salgado
Notes: <<<1.1>>>
###Control System Design###
{{{Control, Design}}}

## Slide 2: Chapter 1
The Excitement of Control Engineering

## Slide 3: Motivation for Control Engineering
Feedback control has a long history which began with the early desire of humans to harness the materials and forces of nature to their advantage. Early examples of control devices include clock regulating systems and mechanisms for keeping wind-mills pointed into the wind.
Modern industrial plants have sophisticated control systems which are crucial to their successful operation.
Notes: <<<1.2>>>

## Slide 4: A modern industrial plant: A section of the OMV Oil Refinery in Austria

## Slide 5
Control Engineering has had a major impact on society. For example, Watt’s Fly Ball Governor had a major impact on the industrial revolution. Indeed, most modern systems (aircraft, high speed trains, CD players, … ) could not operate without the aid of sophisticated control systems.
Notes: <<<1.3>>>

## Slide 6
Figure 1.1: Watt’s fly ball governor
Notes: {{{Flyball Governor}}}

## Slide 7
This photograph shows a flyball
governor used on a steam engine
in a cotton factory near Manchester
in the United Kingdom. Of course,
Manchester was at the centre of the
industrial revolution. Actually, this
cotton factory is still running today.
Notes: {{{cotton mill}}}

## Slide 8
This flyball governor is in the
same cotton factory in Manchester.
However, this particular governor
was used to regulate the speed of
a water wheel driven by the flow of
the river. The governor is quite
large as can be gauged by the outline
of the door frame behind the
governor.

## Slide 9
Improved control is a key enabling technology underpinning:
enhanced product quality
waste minimization
environmental protection
greater throughput for a given installed capacity
greater yield
deferring costly plant upgrades, and
higher safety margins

## Slide 10
Figure 1.2: Process schematic of a Kellogg ammonia plant
All of the above issues are relevant to the control of an
integrated plant such as that shown below.
Notes: {{{ammonia plant}}}

## Slide 11: Types of Control System Design
Control system design also takes several different forms and each requires a slightly different approach.
The control engineer is further affected by where the control system is in its lifecycle, e.g.:
Initial "grass roots" design
Commissioning and Tuning
Refinement and Upgrades
Forensic studies
Notes: <<<1.4>>>
###Types of Control System Design###

## Slide 12: System Integration
Success in control engineering depends on taking a holistic viewpoint. Some of the issues are:
plant, i.e. the process to be controlled
objectives
sensors
actuators
communications
computing
architectures and interfacing
algorithms
accounting for disturbances and uncertainty
Notes: <<<1.5>>>
###System Integration###

## Slide 13: Plant
The physical layout of a plant is an intrinsic part of control problems. Thus a control engineer needs to be familiar with the "physics" of the process under study. This includes a rudimentary knowledge of the basic energy balance, mass balance and material flows in the system.
Notes: <<<1.5.1>>>

## Slide 14: Objectives
Before designing sensors, actuators or control architectures, it is important to know the goal, that is, to formulate the control objectives. This includes
what does one want to achieve (energy reduction, yield increase,...)
what variables need to be controlled to achieve these objectives
what level of performance is necessary (accuracy, speed,...)
Notes: <<<1.5.2>>>

## Slide 15: Sensors
Sensors are the eyes of control enabling one to see what is going on. Indeed, one statement that is sometimes made about control is:
If you can measure it, you can control it.
Notes: <<<1.5.3>>>

## Slide 16: Actuators
Once sensors are in place to report on the state of a process, then the next issue is the ability to affect, or actuate, the system in order to move the process from the current state to a desired state
Notes: <<<1.5.4>>>

## Slide 17
A typical industrial control problem will usually involve many different actuators - see below:
Figure 1.3: Typical flatness control set-up for rolling mill

## Slide 18: A modern rolling mill

## Slide 19: Communications
Interconnecting sensors to actuators, involves the use of communication systems. A typical plant can have many thousands of separate signals to be sent over long distances. Thus the design of communication systems and their associated protocols is an increasingly important aspect of modern control engineering.
Notes: <<<1.5.5>>>

## Slide 20: Computing
In modern control systems, the connection between sensors and actuators is invariably made via a computer of some sort. Thus, computer issues are necessarily part of the overall design. Current control systems use a variety of computational devices including DCS's (Distributed Control Systems), PLC's (Programmable Logic Controllers), PC's (Personal Computers), etc.
Notes: <<<1.5.6>>>

## Slide 21: A modern computer based rapid prototyping system

## Slide 22: Architectures and interfacing
The issue of what to connect to what is a non-trivial one in control system design. One may feel that the best solution would always be to bring all signals to a central point so that each control action would be based on complete information (leading to so called, centralized control). However, this is rarely (if ever) the best solution in practice. Indeed, there are very good reasons why one may not wish to bring all signals to a common point. Obvious objections to this include complexity, cost, time constraints in computation, maintainability, reliability, etc.
Notes: <<<1.5.7>>>

## Slide 23: Table 1.1: Typical control heirarchy

## Slide 24: Algorithms
Finally, we come to the real heart of control engineering i.e. the algorithms that connect the sensors to the actuators. It is all to easy to underestimate this final aspect of the problem.
As a simple example from our everyday experience, consider the problem of playing tennis at top international level. One can readily accept that one needs good eye sight (sensors) and strong muscles (actuators) to play tennis at this level, but these attributes are not sufficient. Indeed eye-hand coordination (i.e. control) is also crucial to success.
Notes: <<<1.5.8>>>

## Slide 25
In summary:
Sensors provide the eyes and actuators the muscle but control science provides the finesse.

## Slide 26
Better Control
Provides more finesse by combining sensors and
actuators in more intelligent ways
Better Actuators
Provide more Muscle
Better Sensors
Provide better Vision

## Slide 27: Disturbances and Uncertainty
One of the things that makes control science interesting is that all real life systems are acted on by noise and external disturbances. These factors can have a significant impact on the performance of the system. As a simple example, aircraft are subject to disturbances in the form of wind-gusts, and cruise controllers in cars have to cope with different road gradients and different car loadings.
Notes: <<<1.5.9>>>

## Slide 28: Homogeneity
A final point is that all interconnected systems, including control systems, are only as good as their weakest element. The implications of this in control system design are that one should aim to have all components (plant, sensors, actuators, communications, computing, interfaces, algorithms, etc) of roughly comparable accuracy and performance.
Notes: <<<1.5.10>>>

## Slide 29
In order to make progress in control engineering (as in any field) it is important to be able to justify the associated expenditure. This usually takes the form of a cost benefit analysis.

## Slide 30: Cost benefit analysis
Typical steps include:
Assessment of a range of control opportunities;
Developing a short list for closer examination;
Deciding on a project with high economic or environmental impact;
Consulting appropriate personnel (management, operators, production staff, maintenance staff etc.);
Identifying the key action points;
Collecting base case data for later comparison;
Deciding on revised performance specifications;
Updating actuators, sensors etc.;
Notes: <<<1.5.11>>>

## Slide 31
Development of algorithms;
Testing the algorithms via simulation;
Testing the algorithms on the plant using a rapid prototyping system;
Collecting preliminary performance data for comparison with the base case;
Final implementation;
Collection of final performance data;
Final reporting on project.
Cost benefit analysis (Contd.)

## Slide 32
Signals and systems terminology
Notes: <<<1.6>>>