## Slide 1: Chapter 5
Analysis of SISO Control Loops
Notes: <<<5.1>>>
###SISO Control Loops###

## Slide 2: Topics to be covered
For a given controller and plant connected in feedback we ask and answer the following questions:
Is the loop stable?
What are the sensitivities to various disturbances?
What is the impact of linear modeling errors?
How do small nonlinearities impact on the loop?
We also introduce several analysis tools; specifically
Root locus
Nyquist stability analysis

## Slide 3: Feedback Structures
We will see that feedback can have many desirable properties such as the capacity to reduce the effect of disturbances, to decrease sensitivity to model errors or to stabilize an unstable system. We will also see, however, that ill-applied feedback can make a previously stable system unstable, add oscillatory behaviour into a previously smooth response or result in high sensitivity to measurement noise.
Notes: <<<5.2>>>

## Slide 4
Figure 5.1: Simple feedback control system

## Slide 5
In the loop shown in Figure 5.1 we use transfer functions and Laplace transforms to describe the relationships between signals in the loop. In particular, C(s) and G0(s) denote the transfer functions of the controller and the nominal plant model respectively, which can be represented in fractional form as:

## Slide 6: Laplace Transforms of System Input and Output
and

## Slide 7
Figure 5.2: Two degree of freedom closed loop

## Slide 8: Nominal Sensitivity Functions
These functions are given specific names as follows:
T0(s) : Nominal complementary sensitivity
S0(t) : Nominal sensitivity
Si0(s) : Nominal input disturbance sensitivity
Su0(s) : Nominal control sensitivity
Notes: <<<5.3>>>
###Sensitivity Functions###
{{{Sensitivity}}}

## Slide 9: Relationship between sensitivities

## Slide 10: Internal Stability
Definition 5.1 (Internal stability). We say that the
nominal loop is internally stable if and only if all eight
transfer functions in the equation below are stable.
Notes: <<<5.4>>>
###Closed Loop Stability###
{{{Stability}}}

## Slide 11: Link to Characteristic Equation
Lemma 5.1 (Nominal internal stability)
Consider the nominal closed loop depicted in Figure 5.2. Then the nominal closed loop is internally stable if and only if the roots of the nominal closed loop characteristic equation
all lie in the open left half plane. We call A0L + B0P the nominal closed-loop characteristic polynomial.

## Slide 12: Stability and Polynomial Analysis
Consider a polynomial of the following form:
The problem to be studied deals with the question of whether that polynomial has any root with nonnegative real part. Obviously, this equation can be answered by computing the n roots of p(s). However, in many applications it is of special interest to study the interplay between the location of the roots and certain polynomial coefficients.
Notes: <<<5.5>>>

## Slide 13: Some Polynomial Properties of Special Interest
Property 1: The coefficient an-1 satisfies
Property 2: The coefficient a0 satisfies
Property 3: If all roots of p(s) have negative real parts, it is necessary that ai > 0, i {0, 1, …, n-1}.
Property 4: If any of the polynomial coefficients is nonpositive (negative or zero), then, one or more of the roots have nonnegative real plant.

## Slide 14: Routh’s Algorithm
The Routh’s algorithm is based on the following numerical array:
Table 5.1: Routh’s array
Notes: {{{Routh Array}}}

## Slide 15
Where
with m0 = (n+2)/2 and m1 = m0-1 for n even and m1 = m0 for n odd. Note that the elements 0,i and 1,i are the coefficients of the polynomials arranged in alternated form. Furthermore

## Slide 16: Result:
Consider a polynomial p(s) given by (5.5.8) and its associated array as in Table 5.1. Then the number of roots with real part greater than zero is equal to the number of sign changes in the first column of the array.

## Slide 17: Root Locus (RL)
Another classical tool used to study stability of equations of the type given above is root locus. The root locus approach can be used to examine the location of the roots of the characteristic polynomial as one parameter is varied.
Consider the following equation
with   0 and M, N have degree m, n respectively.
Notes: <<<5.6>>>
###Root Locus###
{{{Root Locus}}}

## Slide 18
Root locus building rules include:
R1 The number of roots of the equation (1 + F(s) = 0) is equal to max{m,n}. Thus, the root locus has max{m,n} branches.
R2 From (1 + F(s) = 0) we observe that s0 belongs to the root locus (for   0) if and only if

## Slide 19
R3 From equation (1 + F(s) = 0) we observe that if s0 belongs to the root locus, the corresponding value of  is 0 where
R4 A point s0 on the real axis, i.e. s0 , is part of the root locus (for   0), if and only if, it is located to the left of an odd number of poles and zeros (so that R2 is satisfied).
R5 When  is close to zero, then n of the roots are located at the poles of F(s), i.e. at p1, p2, …, pn and, if n < m, the other m - n roots are located at  (we will be more precise on this issue below).

## Slide 20
R6 When  is close to , then m of these roots are located at the zeros of F(s), i.e. at c1, c2, …, cm and, if n > m, the other n - m roots are located at  (we will be more precise on this issue below).
R7 If n > m, and  tends to , then, n - m roots asymptotically tend to , following asymptotes which intersect at (,0), where
The angles of these asymptotes are 1, 2, …, m-n, where

## Slide 21
R8 If n < m, and  tends to zero, then, m-n roots asymptotically tend to , following asymptotes which intersect at (, 0), where
The angles of these asymptotes are 1, 2, … m-n, where
R9 When the root locus crosses the imaginary axis, say at s = jwc, then wc can be computed either using the Routh Hurwitz algorithm, or using the fact that s2 + wc2 divides exactly the polynomial D(s) +  M(s), for some positive real value of .

## Slide 22: Example
Consider a plant with transfer function G0(s) and a feedback controller with transfer function C(s), where
We want to know how the location of the closed loop poles change for  moving in +.

## Slide 23
Figure 5.3: Locus for the closed loop poles when the
controller zero varies

## Slide 24: Nominal Stability using Frequency Response
A classical and lasting tool that can be used to assess the stability of a feedback loop is Nyquist stability theory. In this approach, stability of the closed loop is predicted using the open loop frequency response of the system. This is achieved by plotting a polar diagram of the product G0(s)C(s) and then counting the number of encirclements of the (-1,0) point. We show how this works below.
Notes: <<<5.7>>>
###Stability via Frequency Response###
{{{Nyquist Criterion}}}

## Slide 25: Nyquist Stability Analysis
The basic idea of Nyquist stability analysis is as follows:
assume you have a closed oriented curve Cs in s which encircles Z zeros and P poles of the function F(s). We assume that there are no poles on Cs.
If we move along the curve Cs in a defined direction, then the function F(s) maps Cs into another oriented closed curve, CF in F .

## Slide 26
Illustration: Single zero function and Nyquist path Cs in s
c inside Cs
c outside Cs

## Slide 27: Observations
Case (a): c inside Cs
We see that as s moves clockwise along Cs, the angle of F(s) changes by -2[rad], i.e. the curve CF will enclose the origin in F once in the clockwise direction.
Case (b): c outside Cs
We see that as s moves clockwise along Cs, the angle of F(s) changes by 0[rad], i.e. the curve CF will enclose the origin in F once in the clockwise direction.

## Slide 28: More general result:
Consider a general function F(s) and a closed curve Cs in s . Assume that F(s) has Z zeros and P poles inside the region enclosed by Cs. Then as s moves clockwise along Cs, the resulting curve CF encircles the origin in F Z-P times in a clockwise direction.

## Slide 29
To test for poles in the Right half Plane, we choose Cs as the
following Nyquist path
As s traverses the Nyquist path in s , then we plot a polar plot
of F = G0C. Actually we shift the origin to “-1” so that
encirclements of -1 count the zeros of G0C + 1 in the right
half plane.

## Slide 30: Final Result
Theorem 5.1:
If a proper open loop transfer function G0(s)C(s) has P poles in the open RHP, and none on the imaginary axis, then the closed loop has Z poles in the open RHP if and only if the polar plot G0(sw)C(sw) encircles the point (-1,0) clockwise N=Z-P times.

## Slide 31: Discussion
If the system is open loop stable, then for the closed loop to be internally stable it is necessary and sufficient that no unstable cancellatgions occur and that the Nyquist plot of G0(s)C(s) does not encircle the point (-1,0).
If the system is open loop unstable, with P poles in the open RHP, then for the closed loop to be internally stable it is necessary and sufficient that no unstable cancellations occur and that the Nyquist plot of G0(s)C(s) encircles the point (-1,0) P times counterclockwise.
If the Nyquist plot of G0(s)C(s) passes exactly through the point (-1,0), there exists an w0   such that F(jw0) = 0, i.e. the closed loop has poles located exactly on the imaginary axis. This situation is known as a critical stability condition.

## Slide 32: Figure 5.6: Modified Nyquist path (To account for open loop poles or zeros on the imaginary axis).

## Slide 33
Theorem 5.2 (Nyquist theorem):
Given a proper open loop transfer function G0(s)C(s) with P poles in the open RHP, then the closed loop has Z poles in the open RHP if and only if the plot of G0(s)C(s) encircles the point (-1,0) clockwise N=Z-P times when s travels along the modified Nyquist path.

## Slide 34: Relative Stability: Stability margins and Sensitivity Peaks
In control system design, one often needs to go beyond the issue of closed loop stability. In particular, it is usually desirable to obtain some quantitative measures of how far from instability the nominal loop is, i.e. to quantify relative stability. This is achieved by introducing measures which describe the distance from the nominal open loop frequency response to the critical stability point (-1,0).
Notes: <<<5.8>>>
###Relative Stability###

## Slide 35: Figure 5.7: Stability margins and sensitivity peak
Gain and Phase Margins
Peak Sensitivity
Notes: {{{Gain Margin, Phase Margin}}}

## Slide 36
(a) The gain margin, Mg, and the phase margin Mf are defined as follows (see Figure 5.7):
(b) Peak sensitivity:
Since then S0 is a maximum at the frequency where G0(jw)C(jw) is closest to the point -1. The peak sensitivity is thus 1/ - (see Figure 5.7).

## Slide 37: Figure 5.8: Stability margins in Bode diagrams

## Slide 38: Robustness
So far, we have only considered the effect that the controller has on the nominal closed loop formed with the nominal model for the plant. However, in practice, we are usually interested, not only in this nominal performance, but also the true performance achieved when the controller is applied to the true plant. This is the so called “Robustness” issue. We will show below that the nominal sensitivities do indeed tell us something about the true or achieved sensitivities.
Notes: <<<5.9>>>
###Robust Stability###

## Slide 39: Achieved Sensitivities
We contrast the nominal sensitivities derived previously with the achieved (or true) sensitivities when the controller C(s) is applied to the calibration model, G(s). This leads to the following calibration sensitivities:

## Slide 40: Relationship to Modelling Errors
The achieved sensitivity functions are given in terms of the nominal sensitivities as follows:
Where G(s) is the multiplicative modelling error.

## Slide 41: Robust Stability
We are concerned with the case where the nominal model and the true plant differ. It is then necessary that, in addition to nominal stability, we check that stability is retained when the true plant is controlled by the same controller. We call this property robust stability.

## Slide 42
Theorem 5.3 (Robust stability theorem):
Consider a plant with nominal transfer function G0(s) and true transfer function given by G(s). Assume that C(s) is the transfer function of a controller which achieves nominal internal stability. Also assume that G(s)C(s) and G0(s)C(s) have the same number of unstable poles. Then a sufficient condition for stability of the true feedback loop obtained by applying the controller to the true plant is that ...

## Slide 43
where G(jw) is the frequency response of the multiplicative modeling error (MME).

## Slide 44: Proof: Consider the Nyquist plot for the nominal and the true loop

## Slide 45
From that figure we see that the same number of
encirclements occur if
this is equivalent to


## Slide 46: Example
In a feedback control loop, the open loop transfer function is given by
and the true plant transfer function is
Use the Robust Stability Theorem to obtain a bound on the (unmodelled delay)  which guarantees closed loop stability.

## Slide 47: Figure 5.10: Magnitude of the frequency response of T0(s)G (s) for different values of 
Note that |T0(jw)G(jw)| < 1, w for   1.5.

## Slide 48: Summary
This chapter introduced the fundamentals of SISO feedback control loop analysis.
Feedback introduces a cyclical dependence between controller and system:
  the controller action affects the systems outputs,
  and the system outputs affect the controller action.
Notes: <<<5.10>>>

## Slide 49
Well designed, feedback can
  make an unstable system stable;
  increase the response speed;
  decrease the effects of disturbances;
  decrease the effects of system parameter uncertainties, and more.

## Slide 50
Poorly designed, feedback can
  introduce instabilities into a previously stable system;
  add oscillations into a previously smooth response;
  result in high sensitivity to measurement noise;
  result in sensitivity to structural modeling errors, and more.