## Slide 1: Chapter 23
Model Predictive Control
Notes: <<<23.1>>>
###Model Predictive Control###
{{{Model Predictive Control}}}

## Slide 2: Motivation
All real world control problems are subject to constraints of various types. The most common constraints are actuator constraints (amplitude and slew rate limits). In addition, many problems also have constraints on state variables (e.g. maximal pressures that cannot be exceeded, minimum tank levels, etc).
In many design problems, these constraints can be ignored, at least in the initial design phase. However, in other problems, these constraints are an inescapable part of the problem formulation since the system operates near a constraint boundary.

## Slide 3: Motivation - continued
Chapter 11 described methods for dealing with constraints based on anti-windup strategies. These are probably perfectly adequate for simple problems - especially SISO problems. However, in more complex MIMO problems - especially those having both input and state constraints, it is frequently desirable to have a more formal mechanism for dealing with constraints in MIMO control system design.

## Slide 4: Outline
We describe one such mechanism here based on Model Predictive Control. This has actually been a major success story in the application of modern control. More than 2,000 applications of this method have been reported in the literature - predominantly in the petrochemical area. Also, the method is being increasingly used in electromechanical control problems.

## Slide 5: Advantages of Model Predictive Control
The main advantages of MPC are:
it provides a one-stop-shop for MIMO control in the presence of constraints,
it is one of the few methods that allows one to treat state constraints, and
several commercial packages are available which give industrially robust versions of the algorithms aimed at chemical process control.

## Slide 6: Anti-Windup Revisited
We assume that the complete state of a system is directly measured. Then, if one has a time-invariant model for a system and if the objectives and constraints are time-invariant, it follows that the control policy should be expressible as a fixed mapping from the state to the control. That is, the optimal control policy will be expressible as
for some static mapping h(). What remains is to give a characterization of the mapping h().
Notes: <<<23.2>>>
###Anti-Windup Revisited###
{{{Anti-Windup}}}

## Slide 7
We can think of the anti-windup strategies of Chapter 11 as giving a particular simple (ad-hoc) parameterization of h(). Specifically, if the control problem is formulated, in the absence of constraints, as a linear quadratic regulator, then we know that the unconstrained infinite horizon policy is of the form:

## Slide 8: State Space form of Anti-Windup
The anti-windup form of the above linear controller is
where

## Slide 9: Example
We illustrate by a simple example.
Example 23.1: Consider a continuous-time double integrator plant which is sampled with period =1 second. The corresponding discrete time model is of the form
where

## Slide 10
We choose to use infinite horizon LQR theory to develop the control law. Within this framework, we use the following weighting matrices
We first consider the case when the control is unconstrained.
Then, for an initial condition of x(0) = (-10, 0)T, the output response and input signal are as shown below.

## Slide 11: Unconstrained Responses
Figure 23.1:
Output response
without constraints
Figure 23.2:
Input response
without constraints
Figure 23.3:
Phase plane plot
without constraints

## Slide 12: Constraining the input amplitude
We next assume that the input must satisfy the mild constraint |u(k)|  5. Applying the anti-windup policy leads to the response shown on the next slide.

## Slide 13: Responses with Mild Constraint |u(k)| 5
Figure 23.4:
Output response
with input constraint
|u(k)| 5
Figure 23.5:
Input response
with constraint
|u(k)| 5
Figure 23.6:
Phase plane plot
without constraint
|u(k)| 5

## Slide 14: Observations
The various plots indicate that the simple anti-windup strategy has produced a perfectly acceptable response in this case.
The above example would seem to indicate that one need never worry about fancy methods.

## Slide 15: Making the constraint more severe
Example Continued. Consider the same set up as above, save that the input is now required to satisfy the more severe constraint |u(k)| 1. Notice that this constraint is 10% of the initial unconstrained input. Thus, this is a relatively severe constraint. The simple anti-windup control law now leads to the response shown on the next slide.

## Slide 16
Figure 23.7:
Output response
with constraint |u(k)| 1
Figure 23.8:
Input response
with constraint |u(k)| 1
Figure 23.9:
Phase plane plot
with constraint |u(k)| 1

## Slide 17: Observations
We see that the simple anti-windup strategy is not performing well and, indeed, has resulted in large overshoot in this case.

## Slide 18: Discussion of Example with Severe Constraints
We see that the initial input steps have caused the velocity to build up to a large value. If the control were unconstrained, this large velocity would help us get to the origin quickly. However, because of the limited control authority, the system braking capacity is restricted and hence large overshoot occurs. In conclusion, it seems that the control policy has been too shortsighted and has not been able to account for the fact that future control inputs would be constrained as well as the current control input. The solution would seem to be to try to look-ahead (i.e. predict the future response) and to take account of current and future constraints in deriving the control policy. This leads us to the idea of model predictive control.

## Slide 19: What is Model Predictive Control?
Model Predictive Control is a control algorithm based on solving an on-line optimal control problem. A receding horizon approach is used which can be summarized in the following steps:
(i) At time k and for the current state x(k), solve, on-line, an open-loop optimal control problem over some future interval taking account of the current and future constraints.
(ii) Apply the first step in the optimal control sequence.
(iii) Repeat the procedure at time (k+1) using the current state x(k+1).
Notes: <<<23.3>>>

## Slide 20: Turning the solution into a closed loop policy
The solution is converted into a closed loop strategy by using the measured value of x(k) as the current state. When x(k) is not directly measured then one can obtain a closed loop policy by replacing x(k) by an estimate provided by some form of observer.

## Slide 21: Details for Nonlinear Model
Given a model
the MPC at event (x, k) is computed by solving a constrained optimal control problem:
where
and UN is the set of U that satisfy the constraints over the entire interval [k, k + N - 1]; i.e.

## Slide 22
together with the terminal constraint
Usually U  Rm is convex and compact, X  Rn is convex and closed, and W is a set that can be appropriately selected to achieve stability.

## Slide 23
In the above formulation, the model and cost function are time invariant. Hence, one obtains a time-invariant feedback control law.
Then, the actual control applied at time k is the first element of this sequence, i.e.

## Slide 24: Figure 23.10: Receding horizon control principle

## Slide 25
An alternative view of Receding Horizon optimization is shown on the next slide

## Slide 26: Alternative View of Receding Horizon Control Policy

## Slide 27
The associated literature can be divided into four generations as follows:
First generation (1970’s) - used impulse or step response linear models, quadratic cost function, and ad-hoc treatment of constraints.
Second generation (1980’s) - linear state space models, quadratic cost function, input and output constraints expressed as linear inequalities, and quadratic programming used to solve the constrained optimal control problem.
Third generation (1990’s) - several levels of constraints (soft, hard, ranked), mechanisms to recover from infeasible solutions.
Fourth generation (late 1990’s) - nonlinear problems, guaranteed stability, and robust modifications.

## Slide 28: Stability
A remarkable property of MPC is that one can establish stability of the resultant feedback system (at least with full state information). This is made possible by the fact that the value function of the optimal control problem acts as a Lyapunov function for the closed loop system.
Notes: <<<23.4>>>
###Stability of MPC###
{{{Stability, MPC}}}

## Slide 29: Assumptions
For clarity of exposition, we make the following simplifying assumptions:
A1: An additional constraint is placed on the final state
A2: L(x, u) is positive definite in both arguments.

## Slide 30
Theorem 23.1: Consider the system controlled by the receding horizon MPC algorithm and subject to a terminal constraint. This control law renders the resultant closed loop system globally asymptotically stable.

## Slide 31: Details of Proof
The value function is positive definite and proper (V(x) as ||x|| ). It can therefore be used as a Lyapunov function for the problem. We recall that at event (x, k), MPC solves:
subject to constraints.

## Slide 32: Proof continued:
We denote the optimal open loop control sequence solving PN(x) as
We recall that inherent in the MPC strategy is the fact that the actual control applied at time k is the first value of this sequence; i.e.
Let x(1) = f(x, h(x)) and let x(N) be the terminal state resulting from the application of . Note that we are assuming x(N) = 0.

## Slide 33: Proof continued:
A feasible solution (but not the optimal one) for the second step in the receding horizon computation
PN(x1) is then:
Then the increment of the Lyapunov function on using the true MPC optimal input and when moving from x to x(1) = f(x, h(x)) satisfies:

## Slide 34: Proof continued:
However, since is optimal, we know that
where is the sub-optimal sequence defined earlier. Hence, we have

## Slide 35: Proof continued:
Using the fact that shares (N-1) terms in common with , we can see that the right hand side satisfies:
where we have used the fact that leads to x(N) = 0 by assumption and hence leads to x(N+1) = 0.
Finally we have
When L(x, u) is positive definite in both arguments, then stability follows immediately from the Lyapunov Stability Theorem.


## Slide 36
Beyond the issue of stability, a user of MPC would clearly also be interested in what, if any performance advantages are associated with the use of this algorithm. In an effort to (partially) answer this question, we pause to revisit the earlier example.

## Slide 37: Example Revisited
Consider again the problem described earlier with input constraint |u(k)|  1. We recall that the shortsighted policy led to large overshoot.
Here, we consider the MPC cost function with N = 2 and such that F(x(N)) is the optimal unconstrained infinite horizon cost and is the incremental cost associated with the underlying LQR problem.
Here we consider the constraint on the present and next step. Thus the derivation of the control policy is not quite as shortsighted as was previously the case.

## Slide 38: Results for MPC with constraints applied on first two steps
Figure 23.11:
Output response
using MPC
Figure 23.12:
Input response
using MPC
Figure 23.13:
Phase plane plot
using MPC

## Slide 39: Observations
Comparing these results with those obtained earlier, we see that the performance has been significantly improved. This is because the policy is no longer quite so shortsighted as it previously was. Thus we see that MPC can indeed over performance advantages over the shortsighted anti-windup strategy

## Slide 40: Linear Models with Quadratic Cost Function
Model:
Error:
Combined “disturbance”:
Cost:
Notes: <<<23.5>>>
###MPC for Linear Systems###

## Slide 41
It can be shown that, if the design is unconstrained, J0 is minimized by taking
U = -W-1V
where W and V are functions of A, B, C matrices. V is also a function of the disturbances and desired output.
Magnitude and rate constraints on both the plant input and output can be easily expressed as linear constraints on U of the form
LU  K

## Slide 42: QP Solution
Thus the constrained problem takes the form:
This optimization is a convex problem due to the quadratic cost and linear constraints. Also, standard numerical procedures (called Quadratic Programming algorithms or QP for short) are available to solve this sub-problem.
Notes: {{{Quadratic Programming}}}

## Slide 43: Summary of Key Idea
Solve receding horizontal optimal control problem subject to constraints
Apply first step of control - move forward one step
Stability can be established - terminal constraint of x crucial.

## Slide 44: Example
Uss = 0.33
Plant:
Desired Output:
Steady State Input:
Constraint on Input:

## Slide 45: Results: dashed line - unconstrained input solid line - constrained input found via MPC

## Slide 46: Output Response: Dashed line - response when unconstrained input is saturated and applied to plant Solid line - response obtained from MPC algorithm

## Slide 47: One Degree of Freedom Controller
A one-degree of freedom output feedback controller is obtained by including the set point in the quantities to be estimated. The resultant output feedback MPC strategy is schematically depicted below.
Notes: <<<23.6>>>

## Slide 48: Figure 23.14: One-degree-of-freedom MPC architecture

## Slide 49: Integral Action
An important observation is that the architecture described above gives a form of integral action. In particular y is taken to the set-point ys irrespective of the true plant description (provided a steady state is reached and provided that, in this steady state, u is not constrained).

## Slide 50: Rudder Roll Stabilization of Ships
Here we present a realistic application of model
predictive control to rudder roll stabilization of ships.
It is desirable to reduce the rolling motion of ships produced by wave action so as to prevent cargo damage and improve crew efficiency and passenger comfort. Conventional methods for ship roll stabilization include water tanks, stabilization fins and bilge keels. Another alternative is to use the rudder for roll stabilization as well as course keeping. However, using the rudder for simultaneous course keeping and roll reduction is non-trivial since only one actuator is available to deal with two objectives.
Notes: <<<23.7>>>
###Rudder Roll Stabilization###
{{{Rudder Roll Stabilization}}}

## Slide 51: Constraint
An important issue in this problem is that the rudder mechanism is usually limited in amplitude and slew rate. Hence this is a suitable problem for model predictive control.

## Slide 52: Figure 23.15: Magnitudes and conventions for ship motion description

## Slide 53: The Model
Wave disturbances are usually considered at the output, and the complete model of the ship dynamics including the output equation is of the form:
where only the roll and yaw are typically directly measured i.e. y := [, ]T. dwave is the wave induced disturbance on the output variables.

## Slide 54: Model for Wave Disturbances
The wave disturbances can be characterized in terms of their frequency spectrum. This frequency spectrum can be simulated by using filtered white noise. The filter used to approximate the spectrum is usually a second order one of the form

## Slide 55: Control Objectives
The design objectives for rudder roll stabilization are:
Increase the damping and reduce the roll amplitude
Control the heading of the ship

## Slide 56: Details of the Model
The following model was used for the ship
This system was sampled with a zero order hold
and sampling period of 0.5.

## Slide 57: Details of the Optimization Criterion
Details of the model predictive control optimization criterion were that a standard LQR cost function was employed with
Optimization horizon, N = 20; Control horizon M = 18.

## Slide 58: Estimating the System State
Since only roll, , and yaw, , were assumed to be directly measured, then a Kalman filter was employed to estimate the 5 system states and 2 noise states in the composite model.
The results of applying MPC to this problem are shown on the following slides.
We consider three cases:
(i) No constraints on the rudder
(ii) Rudder constrained to a maximum angle of 30 degrees and a
maximum slew rate of 15 degrees per second
(iii) Rudder constrained to a maximum angle of 20 degrees and
a maximum slew rate of 8 degrees per second.

## Slide 59: Figure 23.16: Ship motion with no constraints on rudder motion

## Slide 60: Figure 23.17: Ship motion when rudder constrained to maximum angle of 30 degrees and maximum slew rate of 15 degrees/sec.

## Slide 61: Figure 23.18: Ship motion when rudder constrained to maximum angle of 20 degrees and maximum slew rate of 8 degrees/sec.

## Slide 62: Observations
We see that MPC offers a satisfactory solution to this problem. Roll motion has been significantly reduced and, when reformulated as part of the problem description, constraints on maximum rudder angle and slew rate have been imposed.

## Slide 63: Summary
MPC provides a systematic procedure for dealing with constraints (both input and state) in MIMO control problems.
It has been widely used in industry.
Remarkable properties of the method can be established, e.g. global asymptotic stability provided certain conditions are satisfied (e.g. appropriate weighting on the final state).
Notes: <<<23.8>>>

## Slide 64
The key elements of MPC for linear systems are:
  state space (or equivalent) model,
  on-line state estimation (including disturbances),
  prediction of future states (including disturbances),
  on-line optimization of future trajectory subject to constraints using Quadratic Programming, and
  implementation of first step of control sequence.

## Slide 65: Embellishments
The results presented in this chapter suggest there is a close connection between MPC and anti-windup provided the demands made on the system are not too severe.
Actually, recent research has shown that there exists a non-trivial region of state space in which MPC and anti-windup are equivalent.
The next slides illustrate this idea.

## Slide 66: Illustrative Example
This is the zero-order hold discretisation (with sampling
period Ts - 0.4 sec.) of the double integrator
Saturation level:
Fixed horizon:

## Slide 67: Regions of State Space: A : Region where no saturation occurs B : Region in which MPC and anti- windup are equivalent.
-4
-3
-2
-1
0
1
2
3
4
-8
-6
-4
-2
0
2
4
6
8
x1
x2
B
A
B

## Slide 68: First Step of MPC starting from a point in state space in which MPC  anti-windup but where input saturation occurs
-2
-1
0
1
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k
u(k)

## Slide 69: Second Step - Note input still saturated
-2
-1
0
1
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k
u(k)

## Slide 70: Third Step - Note input still saturated
-2
-1
0
1
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
u(k)
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k

## Slide 71: Fourth Step - Note that state has entered region in which input is no longer saturated
-2
-1
0
1
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k
u(k)

## Slide 72: Remainder of the response - Note input remains unsaturated
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k
u(k)

## Slide 73: Overlay the anti-windup Solution - Note that MPC and anti-windup give the same solution for this particular initial condition
-2
-1
0
1
2
-1.5
-1
-0.5
0
0.5
1
1.5
x1
x2
0
5
10
15
20
25
-1.5
-1
-0.5
0
0.5
1
1.5
k
u(k)

## Slide 74: Observations
1. It is not surprising that anti-windup performs well in some cases because it can be shown that there is a non-trivial region of state space in which anti-windup and MPC are equivalent.
2. However, caution is needed in interpreting this result. In general, anti-windup is too shortsighted and MPC will perform better.
3. Some of these issues are explored in the problems for readers given in the book.