## Slide 1: Chapter 26
Decoupling
Notes: <<<26.1>>>
###Decoupling###

## Slide 2
An idealized requirement in MIMO control-system design is that of decoupling. If a plant is dynamically decoupled, then changes in the set-point of one process variable lead to a response in that process variable but all other process variables remain constant. The advantages of such a design are intuitively clear: e.g., a temperature may be required to be changed, but it may be undesirable for other variables (e.g., pressure) to suffer any associated transient. Full dynamic decoupling is a very stringent requirement. Thus, in practice, it is more usual to seek dynamic decoupling over some desired bandwidth.

## Slide 3
This chapter describes the design procedures necessary to achieve dynamic decoupling. In particular, we discuss
  dynamic decoupling for stable minimum-phase systems
  dynamic decoupling for stable nonminimum-phase systems
  dynamic decoupling for open-loop unstable systems

## Slide 4
As might be expected, full dynamic decoupling is a strong requirement and is generally not cost-free. We will thus also quantify the performance cost of decoupling by using frequency-domain procedures. These allow a designer to assess a-priori whether the cost associated with decoupling is acceptable in a given application.

## Slide 5
Of course, some form of decoupling is a very common requirement. For example, static decoupling is almost always a design requirement. The question then becomes, over what bandwidth will decoupling (approximately) be asked for? It will turn out that the additional cost of decoupling is a function of open-loop poles and zeros in the right-half plane. Thus if one is restricting decoupling in some bandwidth, then by focusing attention on those open-loop poles and zeros that fall within this bandwidth, one can get a feel for the cost of decoupling over that bandwidth.

## Slide 6
We will also examine the impact of actuator saturation on decoupling. In the case of static decoupling, it is necessary to avoid integrator wind-up. This can be achieved by using methods that are analogous to the SISO case treated in Chapter 11.

## Slide 7: Stable Systems
We first consider the situation in which the open-loop poles of the plant are located in desirable locations. We will employ the affine-parameterization technique described in Chapter 25 to design a controller that achieves full dynamic decoupling.
Notes: <<<26.2>>>
###Stable Systems###

## Slide 8: Stable Systems: Part 1 - Minimum-Phase Case
We refer to the general Q-design procedure outlined in Chapter 25.
To achieve dynamic decoupling, we make the following choice for Q(s).
Where R(s) is the right interactor, and p1(s), p2(s), … pm(s) are stable polynomials chosen to make Q(s) proper. The polynomials p1(s), p2(s), … pm(s) should be chosen to have unit d.c. gain.
Notes: <<<26.2.1>>>
###Minimum-Phase Case###

## Slide 9
We observe that, with the above choice, we achieve the following nominal complementary sensitivity:

## Slide 10
We see that this is diagonal, as required. The associated control-system structure would then be as shown below:
Figure 26.1: IMC decoupled control of stable MIMO plants

## Slide 11
Actually, the above design is not unique. For example, an alternative choice for Q(s) is
where DQ(s) is given by

## Slide 12
Note also that DQ(s) can have the more general structure
where t1(s), t2(s), …, tm(s) are proper stable transfer functions having relative degrees equal to the corresponding column degrees of the left interactor for Go(s). The transfer functions t1(s), t2(s), …, tm(s) should be chosen to have unit d.c. gain.

## Slide 13: Example 26.1
Consider a stable 2  2 MIMO system having the nominal model
Choose a suitable matrix Q(s) to control this plant, using the affine parameterization, in such a way that the MIMO control loop is able to track references of bandwidths less than or equal to 2[rad/s] and 4[rad/s] in channels 1 and 2, respectively.

## Slide 14
We will aim to obtain a complementary sensitivity matrix given by
where T11(s) and T22(s) will be chosen to have bandwidths 2[rad/s] and 4[rad/s] in channels 1 and 2, respectively.

## Slide 15
Then, Q(s) must ideally satisfy
We choose the structure from which we see that To(s) = DQ(s). Hence the relative degrees of T11(s) and T22(s) will be chosen equal to the degrees of the first and second column of the left interactor for Go(s), respectively.

## Slide 16
The left interactor L(s) is
Then

## Slide 17
Hence, Q(s) is proper if and only if To(s) is chosen so as to make L(s)To(s) proper.
Thus, possible choices for T11(s) and T22(s) are

## Slide 18
To obtain the final expression for Q(s), we next need to compute [Go(s)]-1, which is given by

## Slide 19
We finally obtain

## Slide 20
The above design procedure is limited to minimum-phase systems. In particular, it is clear that Q(s), chosen as above, is stable if and only if Go(s) is minimum phase, because [R(s)]-1 and [L(s)]-1 involve an inverse of Go(s). We therefore need to modify Q(s) so as to ensure stability when Go(s) is nonminimum phase. A way of doing this is described below.

## Slide 21: Stable Systems: Part 2 - Nonminimum-Phase Case
We will begin with the state space realization for [R(s)]-1, defined by a 4-tuple (A, B, C, D). We will denote by ũ(t) the input to this system. Our aim is to modify [R(s)]-1 so as to achieve two objectives:
(i) render the transfer function stable, whilst;
(ii) retaining its diagonalizing properties.
Notes: <<<26.2.2>>>
###Nonminimum-Phase Case###

## Slide 22
To this end, we define the following subsystem, which is driven by the ith component of ũ(t)
where i(t)  m, ũi(t)  , and (Ai, Bi, Ci, Di) is a minimal realization of the transfer function from the ith component of ũ(t) to the complete vector output ū(t). Thus (Ai, Bi, Ci, Di) is a minimal realization of (A, Bei, C, Dei), where ei is the ith column of the m  m identity matrix.

## Slide 23
We next apply stabilizing state feedback to each of these subsystems - i.e., we form
where . The design of Ki can be done in any convenient fashion - e.g., by linear quadratic optimization.

## Slide 24
Finally we add together the m vectors 1(t), 2(t), … m(t) to produce an output, which can be renamed ū(t):
We then have the following result:

## Slide 25
Lemma 26.1:
(a) The transfer function from to ū(t) is given by
where
(b) R(s)W(s) is a diagonal matrix.
(c) W(s) has a state space realization as described above.
Proof: See the book.

## Slide 26
Returning now to the problem of determining Q(s), we choose
This is equivalent to
Then

## Slide 27
Finally, we see that the resulting nominal complementary sensitivity is
Note this complementary sensitivity is achieved without requiring any unstable pole-zero cancellations, and that any nonminimum-phase zeros in the plant are retained in To(s), which is a requirement for internal stability.

## Slide 28
The reader will notice that it is implicit in the above design that some of the NMP zeros have been duplicated and appear in multiple diagonal elements. At worst, each NMP zero will appear in every diagonal term. Precisely how many zeros will appear and in which channel, depends on the degree of each minimum realization involved.
This spreading of NMP zeros is one of the costs associated with demanding full diagonal decoupling.

## Slide 29: Decoupling Invariants
Actually, the NMP zeros appearing in
are diagonalizing invariants and appear in all possible diagonalized closed loops. Thus, spreading NMP dynamics into other channels is a trade-off inherently associated with decoupling.
The final implementation of Q(s) is as shown below.

## Slide 30: Figure 26.2: Diagonal decoupling MIMO controller (Q(s))

## Slide 31: Example 26.2
Consider a plant having the nominal model

## Slide 32
This model has a NMP zero at s = 4. To synthesize a controller following the ideas presented above, we first compute a right interactor matrix, which turns out to have the general form R(s) = diag{s + , (s + )2}. For numerical simplicity, we choose  = 1. Then
and a state space realization for [R(s)]-1 is

## Slide 33
We next compute (Ai, Bi, Ci, Di) as a minimal realization of (A, Bei, C, Dei), for i = 1, i = 2. This computation yields

## Slide 34
These subsystems can be stabilized by state feedback with gains K1 and K2, respectively. For this case, each gain is chosen to shift the unstable pole at s = 4 to a stable location, say s = -10, which leads to K1 = K2 = 14. Thus, Dz(s) is a 2  2 diagonal matrix given by

## Slide 35
We finally choose DQ(s) to achieve a bandwidth approximately equal to 3[rad/s], say

## Slide 36
Note that the elements t1(t) and t2(s) in DQ(s) have been chosen of relative degree equal to the corresponding column degrees of the interactor R(s). Also, their d.c. gains have been chosen to yield unit d.c. gain in the complementary sensitivity To(s), leading to

## Slide 37: Pre- and PostDiagonalization
The transfer-function matrix Q(s) presented in
is actually a right-diagonalizing compensator for a stable (but not necessarily minimum-phase) plant. This can be seen by noting that
where
Notes: <<<26.3>>>
###Pre- and Post Diagonalization###

## Slide 38
It is sometimes also desirable to have a left-diagonalizing compensator. We could derive such a compensator from first principles. However, a simple way is to first form
We find a right-diagonalizing compensator for by using the method outlined above. We then let which has the following property.
Which is a diagonal matrix by construction.

## Slide 39: Unstable Systems
We next turn to the problem of designing a decoupling controller for an unstable MIMO plant. Here we have an additional complexity: some minimal feedback is necessary to ensure stability. To gain insight into this problem, we describe four alternative design choices in the book; namely
Notes: <<<26.4>>>
###Unstable Systems###

## Slide 40
(i) a two-degree-of-freedom design based on prefiltering the reference;
(ii) a two-degree-of-freedom design using the affine parameterization;
(iii) a design based on one-degree-of-freedom state feedback; and
(iv) a design integrating both state feedback and the affine parameterization.

## Slide 41: Two-Degree-of-Freedom Design Based on PreFiltering the Reference
If one requires full dynamic decoupling for reference-signal changes only, then this can be readily achieved by first stabilizing the system by using some suitable controller C(s) and then using prefiltering of the reference signal. The essential idea is illustrated on the next slide.
Notes: <<<26.4.1>>>
### Two-Degree-of-Freedom Design Based on PreFiltering the Reference###

## Slide 42: Figure 26.3: Prefilter design for full dynamic decoupling

## Slide 43
Say that the plant has transfer function Go(s); then the closed-loop transfer function linking R(s) to Y(s) is
To achieve decoupling, one then need only choose H(s) as a right-diagonalizing precompensator for the stable transfer function [I + Go(s)C(s)]-1Go(s)C(s).

## Slide 44: Example 26.4
Consider the plant
where

## Slide 45
The state space model for the system is
where
We will design a stabilizing controller under the architecture shown below.

## Slide 46: Figure 26.4: Optimal quadratic design with integral action

## Slide 47
We design an observer for the state xp(t), given the output y(t). This design uses Kalman-filter theory with Q = BoBoT and R = 0.05I22.
The optimal observer gains turn out to be

## Slide 48
We wish to have zero steady-state errors in the face of step input disturbances. We therefore introduce an integrator with transfer function I/s at the output of the system (after the comparator). That is, we add

## Slide 49
We can now define a composite state vector
leading to the composite model
where

## Slide 50
We next consider the composite system and design a state variable feedback controller via LQR theory.
We choose

## Slide 51
Leading to the feedback gain K = [K1 K2], where

## Slide 52
This leads to the equivalent closed loop shown below (where we have ignored the observer dynamics, because these disappear in steady state).
Figure 26.5: Equivalent closed loop (ignoring the observer dynamics)

## Slide 53
The resulting closed-loop responses for unit step references are shown on the next slide where r1(t) = (t - 1) and r2(t) = -(t - 501). Note that, as expected, the system is statically decoupled, but significant dynamic coupling occurs during transients, especially following the step in the second reference.

## Slide 54: Figure 26.6: Statically decoupled control

## Slide 55
We next design a precompensator to achieve full dynamic decoupling for reference signals. The closed loop has the transfer function
where
This is a stable proper transfer function. Note, however, that this is nonminimum phase, because the original plant was nonminimum phase.

## Slide 56
We use the techniques outlined above to design a right inverse that retains dynamic decoupling in the presence of nonminimum-phase zeros. To use those techniques, the equivalent plant is the closed-loop system with transfer function and with state space model given by the 4-tuple (Ae, Be, Ce, 0), where

## Slide 57
A suitable interactor for this closed-loop system is

## Slide 58
This leads to an augmented system having the state space model with

## Slide 59
The exact inverse then has the state space model (A, B, C, D), where

## Slide 60
We now form the two subsystems as described earlier. We form minimal realizations of these two systems, which we denote by (A1, B1, C1, D1) and (A2, B2, C2, D2) . We determine stabilizing feedback for these two systems by using LQR theory with

## Slide 61
We then implement the precompensator as in Figure 26.2, where we choose
where K1, K2 now represent the stabilizing gains for the two subsystems.

## Slide 62
The resulting closed-loop responses for step references are shown on the next slide, where r1(t) = (t - 1) and r2(t) = -(t - 501). Note that, as expected, the system is now fully decoupled from the reference to the output response.

## Slide 63: Figure 26.7: Dynamically decoupled control

## Slide 64
The reader is invited to simulate and study the input/output behavior of the prefilter, H(s). Note the subtly coordinated interaction in the reference signals as seen by the plant (output of H(s)). It would be virtually impossible for a human operator to manipulate the references, by hand, so that one plant output changed without inducing a transient in the the other output.

## Slide 65: Other decoupling designs
It is also possible to obtain the following designs:-
Two-Degree-of-Freedom Design Based on the Affine Parameterization
One-Degree-of-Freedom Design using State Feedback
We leave the reader to explore the details in the book.

## Slide 66: Zeros of Decoupled and Partially Decoupled Systems
We have seen above that NMP zeros and unstable poles significantly affect the ease with which decoupling can be achieved. Indeed, the analysis above suggests that a single RHP zero or pole might need to be dealt with in multiple loops if decoupling is a design requirement. More details are given in the book.
Notes: <<<26.5>>>
### Zeros of Decoupled and Partially Decoupled Systems###

## Slide 67: Frequency-Domain Constraints for Dynamically Decoupled Systems
Further insight into the multivariable nature of frequency-domain constraints can be obtained by examining the impact of decoupling on sensitivity trade-offs.
Consider a MIMO control loop where So(s) and, consequently, To(s) are diagonal stable matrices.
We then have the following theorem which gives an integral constraint on sensitivity when a diagonal decoupling requirement is imposed.
Notes: <<<26.6>>>
### Frequency-Domain Constraints for Dynamically Decoupled Systems###

## Slide 68
Lemma 26.3: Consider a MIMO plant with a NMP zero at s = z0 =  + j, with associated directions h1T, h2T … hzT.
Assume, in addition, that So(s) is diagonal; then, for any value of r such that hir  0,
Proof: See the book.

## Slide 69
Corollary: Under the same hypothesis of the above Lemma, if the MIMO loop is decoupled (diagonal sensitivity matrix) and the design specification is |[So(j)]rr|  rr << 1 for   [0, r], then
Proof: See the book.

## Slide 70
We also have the following corresponding result for the complementary sensitivity function.
Lemma 26.4: Consider a MIMO system with an unstable pole located at s = 0 =  + j and having associated directions, g1, …, gr. Assume, in addition, that To(s) is diagonal; then, for any value of r such that gir  0,
Proof: See the book.

## Slide 71: The Cost of Decoupling
We can now investigate the cost of dynamic decoupling, by comparing the results in Chapter 24 with those in the above results. To make the analysis more insightful, we assume that the geometric multiplicity z of the zero is 1 - i.e., there is only one left direction, h1, associated with the particular zero.
Notes: <<<26.7>>
### The Cost of Decoupling###

## Slide 72
We first assume that the left direction (h1) has more than one element different from zero - i.e., that the cardinality i is larger than one. We then compare the integral constraint applicable in the absence of coupling:
to the following integral constraint
(applicable to a dynamically decoupled MIMO loop).

## Slide 73
In the first equation, we see that the right-hand side of the inequality can be negative for certain combinations of nonzero off-diagonal sensitivities. Thus, it is feasible to use off-diagonal sensitivities to reduce the lower bound on the diagonal sensitivity peak. This can be interpreted as a two-dimensional sensitivity trade-off, because it involves a spatial as well as a frequency dimension.

## Slide 74
We recall that the capacity to use spatial interaction to reduce sensitivity peaks is a feature of MIMO systems. The idea is that sensitivity dirt can be shared between outputs. This is shown in cartoon form on the next slide.

## Slide 75: Spatial Allocation of Sensitivity
Sensitivity dirt
Multiple piles

## Slide 76
The conclusion from the above analysis is that it is less restrictive, from the point of view of design trade-offs and constraints, to have an interacting MIMO control loop, compared to a dynamically decoupled one. However, it is a significant fact that to draw these conclusions we relied on the fact that h1 had more than one nonzero element. If that is not the case, i.e., if only h1r  0 (the corresponding direction is canonical), then there is no additional trade-off imposed by requiring a decoupled closed loop.

## Slide 77: Example
Consider the following MIMO system:
where

## Slide 78: Zeros
The zeros of the plant are the roots of det(GoN(s)) - i.e., the roots of -s6 - 11s5 - 43s4 - 63s3 + 74s + 44. Only one of these roots, namely the one located at s = 1, lies in the RHP. Thus, z0 = 1, and
We then compute Go(1) as
From which it can be seen that the dimension of the null space is z = 1 and the (only) associated (left) direction is hT = [5 - 6].

## Slide 79
Clearly, this vector has two nonzero elements, so we could expect that there will be additional design trade-offs arising from decoupling. (The direction of the RHP zero is not canonical).

## Slide 80
Using the earlier theorem for r = 1 and r = 2, we obtain, respectively for the non diagonally coupled case:

## Slide 81
If we impose typical design requirements, we have, for the interacting MIMO loop, that

## Slide 82
If we require dynamic decoupling, the sensitivity integrals become
With dynamic decoupling and typical design requirements, we have

## Slide 83
To quantify the relationship between the magnitude of the bounds in the coupled and the decoupled situations, we use an indicator 1d, formed as the quotient between the right-hand sides of inequalities
and

## Slide 84
It follows that the indicator of the cost of decoupling is given by:
Thus, 1 is a relative measure of interaction in the direction from channel 1 to channel 2.

## Slide 85
The issues discussed above are captured in graphical form in the following figure.
Figure 26.10: Cost of decoupling in terms of sensitivity-peak lower bounds

## Slide 86
In the above figure, we show a family of curves, each corresponding to a different bandwidth c. Each curve represents, for the specified bandwidth, the ratio between the bounds for the sensitivity peaks as a function of the decoupling indicator, 1. We can summarize our main observations as follows:
a) When 1 is very small, there is virtually no effect of channel 1 into channel 2 (at least in the frequency band [0, c]); then, the bounds are very close (1d  1).

## Slide 87
b) As 1 increases, we are allowing the off-diagonal sensitivity to become larger than the diagonal sensitivity in [0, c]). The effect of this manifests itself in 1d < 1, i.e. in bounds for the sensitivity peak that are smaller than for the decoupled situation.
c) If we keep 1 fixed and we increase the bandwidth, then the advantages of using a coupled system also grow.

## Slide 88
We see, from the above example, that decoupling can be relatively cost-free, depending upon the bandwidth over which one requires that the closed-loop system operate. This is in accord with intuition, because zeros become significant only when one pushes the bandwidth beyond their locations.

## Slide 89
We illustrate this conclusion for the system described above.
Consider the plant
which has an ORHP zero at s = 1 with output direction equal to * = [5, -6].
Since this direction is not canonical, we can argue from the preceding discussion that there will be a cost in sensitivity associated with achieving diagonal decoupling.

## Slide 90
If we require |Sik(j)|  ik, for  in [-1, 1], i = 1, 2, then
Constraints on S11 harden as the system is more decoupled.
RHS as a function of 11, for 1 = 0.3 and for: 21 = 0, 0.01, 0.05, 0.1 (plots 1 to 4).

## Slide 91
We now apply a particular design technique, (we will not go into details of the design, but  = 1 gives full dynamic decoupling and  = 0 gives a triangular design) that allows different degrees of decoupling while keeping other design parameters essentially constant. The resultant S is

## Slide 92
The next slide shows the effect of the extent of decoupling (measured by ) on the magnitude of the sensitivity S11(j).

## Slide 93
Effect of decoupling on S11(j)
We see that the closer we are to full decoupling the
greater the peak in sensitivity.

## Slide 94: Summary of Cost of Decoupling
Depending on directionality properties of the zero-pole structure of the plant, design constraints in MIMO may relax with respect to the SISO case (the cost of ORHP zeros and poles is distributed in S or T).
If the zero direction is not canonical, there is an additional cost associated to decoupling, as restrictions concentrate on the diagonal elements.
If the zero direction is canonical, the system is structurally equivalent to the SISO system, in terms of constraints. There is no additional cost associated with decoupling.

## Slide 95: Input Saturation
Finally, we explore the impact that input saturation has on linear controllers that enforce decoupling. We will also develop anti-wind-up mechanisms that preserve decoupling in the face of saturation, using methods that are the MIMO equivalent of the SISO anti-wind-up methods of Chapter 11.
Notes: <<<26.8>>>
###Input Saturation###

## Slide 96
We assume that our plant is modeled as a square system, with input u(t)  m and output y(t)  m. We also assume that the plant input is subject to saturation. Then if u(i)(t) corresponds to the plant input in the ith channel, i = 1, 2, …, m, the saturation is described by

## Slide 97
For simplicity of notation, we further assume that the linear region is symmetrical with respect to the origin, i.e. i = 1, 2, …, m. We will describe the saturation levels by usat  m, where
The essential problem with input constraints, as in Chapter 11, is that the control signal can wind up during periods of saturation.

## Slide 98: MIMO Anti-Wind-Up Mechanism
In Chapter 11, the wind-up problems were dealt with by using a particular implementation of the controller. This idea can be easily extended to the MIMO case, as follows.
Assume that the controller transfer-function matrix, C(s), is biproper- i.e.,
where C is nonsingular. The multivariable version of the anti-wind-up scheme if as shown on the next slide.
Notes: <<<26.9>>>
###MIMO Anti-Wind-Up Mechanism###

## Slide 99: Figure 26.11: Anti-wind-up controller implementation. MIMO case

## Slide 100
In the scalar case, we found that the nonlinear element could be thought of in many different ways - e.g., as a simple saturation or as a reference governor. However, for SISO problems, all these procedures turn out to be equivalent. In the MIMO case, subtle issues arise from the way that the desired control, û(t), is projected into the allowable region. We will explore three possibilities.
(i) simple saturation
(ii) input scaling
(iii) error scaling

## Slide 101
Simple saturation: Input saturation is the direct analog of the scalar case.
Input scaling: Here, compensation is achieved by scaling down the controller output vector û(t) to a new vector û(t), every time that one (or more) component of û(t) exceeds its corresponding saturation level. The scaling factor, , is chosen in such a way that u(t) = û(t) - i.e., the controller is forced to come back just to the linear operation zone. This idea is shown schematically below.

## Slide 102: Figure 26.12: Scheme to implement the scaling of controller outputs
(In the above figure C1 should be C)

## Slide 103
Error scaling: The third scheme is built by scaling the error vector down to bring the loop just into the linear region. We refer to the following slide.

## Slide 104: Figure 26.13: Implementation of anti-wind-up via error scaling
(In the above figure C1 should be C)

## Slide 105
Note that û can be changed only instantaneously by modifying w2, because w1(t) is generated through a strictly proper transfer function. Hence, the scaling of the error is equivalent to bringing w2 to a value such that û is just inside the linear region.

## Slide 106
In Figure 26.13, the block f denotes a function that generates the scaling factor 0 <  < 1. We observe that the block with transfer-function matrix [C(s)-1] - C is strictly proper, so that any change in the error vector e(t) will translate immediately into a change in the vector û(t). Instead of introducing abrupt changes in e(t) (and thus in û(t), a gentler strategy can be used. An example of this strategy is to generate  as the output of a first-order dynamic system with unit d.c. gain, time constant , and initial condition (0) = 1.

## Slide 107: Figure 26.14: Effects of different techniques for dealing with saturation in MIMO systems
û : raw control signal
us : control signal which results from directly saturating u(1)
uu : control signal obtained with the scaled control technique (as in Figure 26.12)
ue : control signal obtained with the scaled error technique (as in Figure 26.13)

## Slide 108: Example
Consider a MIMO process having the nominal model
with

## Slide 109
Note that this model is stable and minimum phase. Therefore, dynamic decoupling is possible without significant difficulties.
A suitable decoupling controller is

## Slide 110
We first run a simulation that assumes that there is no input saturation. The results are shown below. Observe that full dynamic decoupling has indeed been achieved.
Figure 26.15: Decoupled design in the absence of saturation

## Slide 111
We run a second simulation including saturation for the controller output in the first channel, at symmetrical levels ±2.5. The results are shown below
Figure 26.16: Linear decoupled design - saturation in channel 1, at ±2.5.

## Slide 112
Clearly, the results are very poor. This is due to wind-up effects and stray coupling in the controller that occur during saturation but which have not been compensated. We therefore explore anti-wind-up procedures.
We example the three anti-wind-up procedures described above.

## Slide 113
Simple saturation: The results of simply putting a saturation element into the nonlinear element of the MIMO anti-windup current are shown on the next slide. It can be seen that this is unsatisfactory - indeed, the results are similar to those where no anti-wind-up mechanism was used.

## Slide 114: Figure 26.17: Decoupled linear design with saturation in channel 1 and anti-wind-up scheme

## Slide 115
Input scaling: A rather disappointing result is observed regarding the plant outputs. They are shown on the next slide.
The results show only a marginal improvement over those obtained by using the pure anti-wind-up mechanism.

## Slide 116: Figure 26.19: Plant outputs when using control scaling

## Slide 117
Error scaling: When the error-scaling strategy is applied to our example, we obtain the results shown on the next slide.

## Slide 118: Figure 26.20: Plant outputs when using scaled errors

## Slide 119
The results are remarkably better than those produced by the rest of the strategies treated so far. Actually, full dynamic decoupling is essentially retained here - the small coupling evident, is due to the implementation of the error scaling via a (fast) dynamical system.

## Slide 120: Summary
Recall these key closed-loop specifications shared by SISO and MIMO design:
  continued compensation of disturbances
  continued compensation of model uncertainty
  stabilization of open-loop unstable systems
whilst not
  becoming too sensitive to measurement noise
  generating excessive control signals
and accepting inherent limitations due to
  unstable zeros
  unstable poles
  modeling error
  frequency- and time-domain integral constraints
Notes: <<<26.10>>>
### Summary###

## Slide 121
Generally, MIMO systems also exhibit additional complexities due to
  directionality (several inputs acting on one output)
  dispersion (one input acting on several outputs)
  and the resulting phenomenon of coupling.
Designing a controller for closed-loop compensation of this MIMO coupling phenomenon is called decoupling.
Recall that there are different degrees of decoupling, including the following:
  static (i.e., To(0) is diagonal);
  triangular (i.e., To(s) is triangular); and
  dynamic (i.e., To(s) is diagonal).

## Slide 122
Due to the fundamental law that So(s) + To(s) = I, if To exhibits any of these decoupling properties, so does So.
The severity and types of the trade-offs associated with decoupling depend on
  whether the system is minimum phase;
  the directionality and cardinality of nonminimum-phase zeros;
  unstable poles.
If all of the system’s unstable zeros are canonical (their directionality affects one output only), then their adverse effect is not spread to other channels by decoupling, provided that the direction of decoupling is congruent with the direction of the unstable zeros.

## Slide 123
The price for dynamically decoupling a system having noncanonical nonminimum-phase zeros of simple multiplicity is that
  the effect of the nonminimum-phase zeros is potentially spread across several loops; and,
  therefore, although the loops are decoupled, each of the affected loops needs to observe the bandwidth and sensitivity limitations imposed by the unstable zero dynamics.
If one accepts the less stringent triangular decoupling, the effect of dispersing limitations due to nonminimum-phase zeros can be minimized.

## Slide 124
Depending on the case, a higher cardinality of nonminimum-phase zeros can either enforce or mitigate the adverse effects.
If a system is also open-loop unstable, there may not be any way at all to achieve full dynamic decoupling with a one-d.o.f. controller, although it is always possible with a two-d.o.f. architecture for reference-signal changes.
If a system is essentially linear but exhibits such actuator nonlinearities as input or slew-rate saturations, then the controller design must reflect this appropriately.

## Slide 125
Otherwise, the MIMO generalization of the SISO wind-up phenomenon can occur.
MIMO wind-up manifests itself in two aspects of performance degradation:
  transients due to growing controller states; and
  transients due to the nonlinearity impacting on directionality.

## Slide 126
The first of these two phenomena …
  … is analogous to the SISO case.
  … is due to the saturated control signals not being able to annihilate the control errors sufficiently fast compared to the controller dynamics; therefore the control states continue to grow in response to the nondecreasing control. These wound up states produce the transients when the loop emerges from saturation.
  … can be compensated by a direct generalization of the SISO anti-wind-up implementation.
The second phenomena …
  … is specific to MIMO systems.
  … is due to uncompensated interactions arising from the input vectors losing its original design direction.

## Slide 127
Analogously to the SISO case, there can be regions in state space from which an open-loop unstable MIMO system with input saturation cannot be stabilized by any control.
More severely than in the SISO case, MIMO systems are difficult to control in the presence of input saturation, even if the linear loop is stable and the controller is implemented with anti-wind-up. This is due to saturation changing the directionality of the input vector.
This problem of preserving decoupling in the presence of input saturation can be addressed by anti-wind-up schemes that scale the control error rather than the control signal.