## Slide 1: Chapter 16
Control Design Based on Optimization
Notes: <<<16.1>>>
###Control Design Based on Optimization###

## Slide 2
Thus far, we have seen that design constraints arise from a number of different sources:
structural plant properties, such as NMP zeros or unstable poles;
disturbances - their frequency content, point of injection, and measurability;
architectural properties and the resulting algebraic laws of trade-off; and
integral constraints and the resulting integral laws of trade-off.

## Slide 3
The subtlety as well as complexity of the emergent trade-off web, into which the designer needs to ease a solution, motivates interest in what is known as criterion-based control design or optimal control theory: the aim here is to capture the control objective in a mathematical criterion and solve it for the controller that (depending on the formulation) maximizes or minimizes it.

## Slide 4
Three questions arise:
1. Is optimization of the criterion mathematically feasible?
2. How good is the resulting controller?
3. Can the constraint of the trade-off web be circumvented by optimization?

## Slide 5: Optimal Q Synthesis
In this chapter, we will combine the idea of Q synthesis with a quadratic optimization strategy to formulate the design problem.
This approach is facilitated by the fact, already observed, that the nominal sensitivity functions are affine functions of Q(s).
Notes: <<<16.2>>>
###Optimal Q Synthesis###

## Slide 6
Assume that a target function H0(s) is chosen for the complementary sensitivity T0(s). We have seen in Chapter 15 that, if we are given some stabilizing controller C(s) = P(s)/L(s), then all stabilizing controllers can be expressed as
the nominal complementary sensitivity function is then given by

## Slide 7
where H1(s) and V(s) are stable transfer functions of the form
We see that T0 is linear in the design variable Qu. We will use a quadratic optimization criterion to design Qu. The design problem is formally stated on the next slide.

## Slide 8: Quadratic Optimal Synthesis
Let S denote the set of all real rational stable transfer functions; then the quadratic optimal synthesis problem can be stated as follows:
Problem (Quadratic optimal synthesis problem). Find such that
Notes: <<<16.2.2>>>
###Quadratic Optimal Synthesis###

## Slide 9
The criterion on the previous slide uses the quadratic norm, also called the H2-norm, of a function X(s) defined as

## Slide 10
To solve this problem, we first need a preliminary result that is an extension of Pythagoras’ theorem.
Lemma 16.1: Let S0  S be the set of all real strictly proper stable rational functions, and let be the set of all real strictly proper rational functions that are analytical for {s}0. Furthermore assume that Xs(s)  S0 and Xu(s)  . Then
Proof: See the book.

## Slide 11
To use the above result, we will need to split a general function X(s) into a stable part Xs(s) and an unstable part Xu(s). We can do this via a partial-fraction expansion. The stable poles and their residues constitute the stable part.

## Slide 12
We note that the cost function of interest here has the general form
where W(s) = H0(s) - H1(s), H0(s) is the target complementary sensitivity, and H1(s) and V(s) are as below:

## Slide 13: Solution to the Quadratic Synthesis Problem
Lemma 16.2: Provided that V(s) has no zeros on the imaginary axis, then
where
such that Vm(s) is a factor with poles and zeros in the open LHP and Va(s) is an all-pass factor with unity gain, and where [X]s denotes the stable part of X.
Proof: Essentially uses Lemma 16.1 - see the book.

## Slide 14
The solution will be proper only either if V has relative degree zero or if both V has relative degree one and W has relative degree of at least one. However, improper solutions can readily be turned into approximate proper solutions by adding an appropriate number of fast poles to

## Slide 15
Returning to the problem posed earlier, we see that Lemma 16.2 provided an immediate solution, by setting

## Slide 16
The above procedure can be modified to include a weighting function (j). In this framework, the cost function is now given by
No additional difficulty arises, because it is enough to simply redefine V(s) and W(s) to convert the problem into the form

## Slide 17
It is also possible to restrict the solution space to satisfy additional design specifications. For example, forcing an integration is achieved by parameterizing Q(s) as and introducing a weighting function (s) = 1/s. (H0(0) = 1 is also required). This does not alter the affine nature of T0(s) on the unknown function. Hence, the synthesis procedure developed above can be applied, provided that we first redefine the function, V(s) and W(s).

## Slide 18: Example 16.1: Unstable Plant
Consider a plant with nominal model
Assume that the target function for T0(s) is given by

## Slide 19
We first choose the observer polynomial E(s) = (s+4)(s+10) and the controller polynomial F(s) = s2 + 4s + 9.
We then solve the pole-assignment equation A0(s)L(s) + B0(s)P(s) = E(s)F(s) to obtain the prestabilizing control law expressed in terms of P(s) and L(s). The resultant polynomials are

## Slide 20
Now consider any controller from the class of stabilizing control laws as parameterized in
The quadratic cost function is then as in

## Slide 21
Consequently
The optimal Qu(s) is then obtained

## Slide 22
We observe that is improper. However, we can approximate it by a suboptimal (but proper) transfer function, by adding one fast pole to
:

## Slide 23: Example 16.2: Nonminimum-phase Plant
Consider a plant with nominal model
It is required to synthesize, by using H2 optimization, a one-d.o.f. control loop having the target function
and to provide exact model inversion at  = 0.

## Slide 24
The appropriate cost function is defined as
Then the cost function takes the form
where

## Slide 25
We first note that
The optimal can then be obtained by using
from this Q0(s) can be obtained as One fast pole has to be added to make this function proper.

## Slide 26: Robust Control Design with Confidence Bounds
We next show briefly how optimization methods can be used to change a nominal controller so that the resultant performance is robust against model errors.
For the sake of argument we will use statistical confidence bounds - although other types of modelling error can also be used.
Notes: <<<16.3>>>
###Robust Control Design###

## Slide 27: Statistical Confidence Bounds
We have argued in Chapter 3 that no model can give an exact description of a real process.
Our starting point will be to assume the existence of statistical confidence bounds on the modeling error.
In particular, we assume that we are given a nominal frequency response, G0(j), together with a statistical description of the associated errors of the form
where G(j) is the true (but unknown) frequency response and G(j), as usual, represents the additive modeling error.
Notes: <<<16.3.1>>>
###Statistical Confidence Bounds>>>

## Slide 28
We assume that G possesses the following probabilistic properties:
(s) is the stable, minimum-phase spectral factor. Also, is the given measure of the modeling error.
The function  would normally be obtained from some kind of identification procedure.

## Slide 29: Robust Control Design
Based on the nominal model G0(j), we assume that a design is carried out that leads to acceptable nominal performance. This design will typically account for the usual control-design issues such as nonminimum-phase behavior, the available input range, and unstable poles. Let us say that this has been achieved with a nominal controller C0 and that the corresponding nominal sensitivity function is S0. Of course, the value S0 will not be achieved in practice, because of the variability of the achieved sensitivity, S, from S0.
Notes: <<<16.3.2>>>
###Robust Control Design###

## Slide 30
Let us assume, to begin, that the open-loop system is stable. We can thus use the simple form of the parameterization of all stabilizing controllers to express C0 and S0 in terms of a stable parameter Q0.

## Slide 31
The achieved sensitivity, S1, when the nominal controller C0 is applied to the true plant is given by
where G is the additive model error.

## Slide 32
Our proposal for robust design now is to adjust the controller so that the distance between the resulting achieved sensitivity, S1, and S0 is minimized. If we change Q0 to Q and hence C0 to C, then the achieved sensitivity changes to

## Slide 33
Where
and
Observe that S1 denotes, the sensitivity achieved when the plant is G0 and the controller is parameterized by Q, and S0 denotes the sensitivity achieved when the plant is G0 and the controller is parameterized by Q0.

## Slide 34: Pictorially
Ge - Random Variable
describing uncertainty
Design Criterion
S0
S1
S2
C0
G0
C0
G0
Ge
C1
G0
Ge

## Slide 35: Frequency Weighted Errors
Unfortunately, (S2 - S0) is a nonlinear function of Q and G.
In place of minimizing some measure of the sensitivity error, we instead consider a weighted version with W2 = 1+GQ. Thus, consider
where is the desired adjustment in Q0(s) to account for G(s).
Notes: <<<16.3.3>>>
###Frequency Weighted Errors###

## Slide 36
The procedure that we now propose for choosing is to find the value that minimizes

## Slide 37
This loss function has intuitive appeal. The first term on the right-hand side represents the bias error. It can be seen that this term is zero if (i.e., we leave the controller unaltered). The second term represents the variance error. This term is zero if - i.e. if we choose open-loop control. These observations suggest that there are two extreme cases. For (no model uncertainty), we leave the controller unaltered; as (large model uncertainty), we choose open-loop control, which clearly is robust for the case of an open-loop stable plant.

## Slide 38: Intuitive Interpretation (Stable Case)
Uncertainty
Bias Term
Variance Term
Due to using Q  Q0
in nominal case
Hence: Bias/Variance Trade-Off

## Slide 39
The robust design is described in:
Lemma 16.4: Suppose that
(i) G0 is strictly proper with no zeros on the imaginary axis and
(ii) E{G(j)G(-j)} has a spectral factorization.
Then (s)(-s)S0(s)S0(-s) + G0(s)G0(-s) has a spectral factor, which we label H, and the optimal is given by

## Slide 40
Proof: Uses Lemma 16.2 - see the book.

## Slide 41
The value of found in Lemma 16.4 gives an optimal trade-off between the bias error and the variance term.

## Slide 42
A final check on robust stability (which is not automatically guaranteed by the algorithm) requires us to check that |G(j)||Q(j) < 1 for all  and all likely values of G (j ). A procedure for doing this is described in the book.

## Slide 43: Incorporating Integral Action
The methodology given above can be extended to include integral action. Assuming that Q0 provides this property, the final controller will do so as well, if has the form
with strictly proper.
There are a number of ways to enforce this constraint. A particularly simply way is to change the cost function to
Notes: <<<16.3.4>>>
###Incorporating Integral Action###

## Slide 44
Lemma 16.5: Suppose that
(I) G0 is strictly proper with no zeros on the imaginary axis and
(ii) E{G(j)G(-j)} has a spectral factorization as in
Then (s)(-s)S0(s)S0(-s) + G0(s)G0(-s) has a spectral factor, which we label H, and
Proof: See the book.

## Slide 45: A Simple Example
Consider a first-order system having constant variance for the model error in the frequency domain:
Notes: <<<16.3.5>>>
###an Example###

## Slide 46: (a) Without integral-action constraint
In this case, with 1 and 2 appropriate functions of 0, cl, and , we can write

## Slide 47
Then there exist A1, A2, A3, and A4, also appropriate functions of 0, cl, and , so that
the optimal is then

## Slide 48
To illustrate this example numerically, we take 0 = 1, cl = 0.5, and  = 0.4. Then we obtain the optimal as

## Slide 49
It is interesting to investigate how this optimal contributes to the reduction of the loss function.

## Slide 50
If then
and if the optimal is used, then the total error is J = 4.9, which has a bias error of
and a variance error of

## Slide 51: (b) With integral-action constraint
We write
The optimal is given by

## Slide 52
For the same set of process parameters as above, we obtain the optimal as
and for Q for controller implementation is simply

## Slide 53: (c) Closed-loop system-simulation results
For the same process parameters as above, we now examine how the robust controller copes with plant uncertainty by simulating closed-loop responses with different processes, and we compare the results for the cases when Q0 is used. We choose the following three different plants.
Case 1:
Case 2:
Case 3:

## Slide 54
The frequency responses of the three plants are shown in Figure 16.1. They are within the statistical confidence bounds centered at G0(j) and have standard deviation of

## Slide 55: Figure 16.1: Plane frequency response: Case 1 (solid); case 2 (dashed); case 3 (dotted)

## Slide 56
Figures 16.2, 16.3 and 16.4 (see next 3 slides), show the closed-loop responses of the three plants for a unit set-point change, controlled by using C and C0.

## Slide 57: Figure 16.2: Closed-loop responses for case 1: when using Q0 (thin line), and when using optimal Q (thick line).

## Slide 58: Figure 16.3: Closed-loop responses for case 2: when using Q0 (thin line), and when using optimal Q (thick line)

## Slide 59: Figure 16.4: Closed-loop responses for case 3: when using Q0 (thin line), and when using optimal Q (thick line)

## Slide 60: Discussion
Case 1: G1(s) = G0(s), so the closed-loop response based on Q0 for this case is the desired response, as specified. The existence of causes degradation in the nominal closed-loop performance, but this degradation is reasonably small, as can be seen from the closeness of the closed-loop responses. This is the price one pays for including a robustness margin aimed at decreasing sensitivity to modeling errors.

## Slide 61
Case 2: There is a large model error between G2(s) and G0(s), shown in figure 16.1. It is seen from Figure 16.3 that, without the compensation of optimal , the closed-loop system and achieves acceptable closed-loop performance in the presence of this large model uncertainty.

## Slide 62
Case 3: Although there is a large model error between G3(s) and G0(s) in the low-frequency region, this model error is less likely to cause instability of the closed-loop system. Figure 16.4 illustrates that the closed-loop response speed, when using the optimal , is indeed slower than the response speed from Q0, but the difference is small.

## Slide 63: Unstable Plant
We next briefly show how the robust design method can be extended to the case of an unstable open-loop plant. As before, we denote the nominal model by , the nominal controller by the nominal sensitivity by S0. We parameterize the modified controller by:
where Q(s) is a stable proper transfer function.
Notes: <<<16.3.6>>>
###Unstable Plant###

## Slide 64
It follows that

## Slide 65
Where G(s) and G(s) denote, as usual, the MME and
AME, respectively.

## Slide 66
As before, we used a weighted measure of S2(s) - S0(s), where the weight is now chosen as
In this case

## Slide 67
We express the additive modeling error G(s) in the form:

## Slide 68
Thus
We can then proceed essentially as in the open-loop stable case.

## Slide 69
We illustrate the above ideas below on a practical system. (A laboratory scale heat exchanger). Note that this system is open-loop stable.

## Slide 70: Practical Example: Laboratory Heat Exchanger

## Slide 71
Motor
Fan
Controllable
Heat
Source
Heating Bed
MV
PV
Temperature Sensor
Air Flow
Pictorial View of Heat Exchanger

## Slide 72: Approximate Model
Based on physical experiments, the model is of the
form:

## Slide 73: System Identification
An experiment was carried out to estimate the model. The resultant input/output data is shown on the next slide.

## Slide 74: Plant Input-Output Data

## Slide 75: Error Bounds
The estimated normal frequency response together with error bounds are shown on the next slide.

## Slide 76: Estimated Frequency Response

## Slide 77: Nominal Model and Controller
Estimated Model
Nominal Controller
in Youla Form

## Slide 78: Stage 2: Robust Control Design
Use Model Error Quantification accounting for noise and undermodelling to modify the controller.
Result is:

## Slide 79: Step Responses with Nominal and robust Controllers
Nominal
Robust
Operating
Point #1
Operating
Point #2

## Slide 80
We see from the above results that the robust controller gives (slightly) less sensitivity of the design to operating point.

## Slide 81: Cheap Control Fundamental Limitations
We next use the idea of quadratic optimal design to revisit the issue of fundamental limitations.
Consider the standard single-input single-output feedback control loop shown, for example, in Figure 5.1 on the next slide.
Notes: <<<16.4>>>
###Cheap Control Fundamental Limitations###

## Slide 82: Figure 5.1:

## Slide 83: Cheap Control
We will be interested in minimizing the quadratic cost associated with the output response expressed by:
Note that, no account is taken here of the size of the control effort. Hence, this class of problem, is usually called cheap control. It is obviously impractical to allow arbitrarily large control signals. However, by not restricting the control effort, we obtain a benchmark against which other, more realistic, scenarios can be judged. Thus these results give a fundamental limit to the achievable performance.

## Slide 84
We will consider two types of disturbances, namely
(i) (impulsive measurement noise (dm(t) = (t)), and
(ii) a step-output disturbance (d0(t) =(t)).
We then have the following result that expresses the connection between the minimum achievable value for the cost function
and the open-loop properties of the system.

## Slide 85
Theorem 16.1: Consider the SISO feedback control loop and the cheap control cost function. Then
(i) For impulsive measurement noise, the minimum value for the cost is
where pi, …, pN, denote the open-loop plant poles in the right half plane, and

## Slide 86
(ii) For a step-output disturbance, the minimum value for the cost is
where c1, …, cM denote the open-loop plant zeros in the right-half plane.
Proof: See the book.

## Slide 87: Frequency-Domain Limitations Revisited
We saw earlier in Chapter 9 that the sensitivity and complementary sensitivity functions satisfied the following integral equations in the frequency domain
(i)
where kh denotes lims 0sH0l(s) and H0l(s) is the open- loop transfer function.
Notes: <<<16.5>>>
###Frequency-Domain Limitations Revisited###

## Slide 88
(ii)
where kv = lims 0sH0l(s).
There is clearly a remarkable consistency between the right-hand sides of the above equations and the results for cheap control. This is not a coincidence as shown in the following result:

## Slide 89
Theorem 16.2: Consider the standard SISO control loop in which the open-loop transfer function H0l(s) is strictly proper and H0l(0)-1 = 0 (i.e. there is integral action), then
(i) for impulse measurement noise, the following inequality holds:
where pi, …, pN denote the plant right-half plane poles.

## Slide 90
(ii) for impulse a unit-step output disturbance, then
where ci, …, cM denote the plant right-half plane poles.
Proof: See the book.

## Slide 91: Summary
Optimization can often be used to assist with certain aspects of control-system design.
The answer provided by an optimization strategy is only as good as the question that has been asked - that is, how well the optimization criterion captures the relevant design specifications and trade-offs.
Optimization needs to be employed carefully: keep in mind the complex web of trade-offs involved in al control-system design.
Notes: <<<16.6>>>
###Summary###

## Slide 92
Quadratic optimization is a particularly simple strategy and leads to a closed-form solution.
Quadratic optimization can be used for optimal Q synthesis.
We have also shown that quadratic optimization can be used effectively to formulate and solve robust control problems when the model uncertainty is specified in the form of a frequency-domain probabilistic error.

## Slide 93
Within this framework, the robust controller biases the nominal solution so as to create conservatism, in view of the expected model uncertainty, while attempting to minimize affecting the achieved performance.
This can be viewed as a formal way of achieving the bandwidth reduction that was discussed earlier as a mechanism for providing a robustness gap in control-system design.