## Slide 1: Chapter 2
Introduction to the Principles of Feedback
Topics to be covered include:
An industrial motivational example;
A statement of the fundamental nature of the control problem;
The idea of inversion as the central ingredient in solving control problems;
Evolution from open loop inversion to closed loop feedback solutions.
Notes: <<<2.1>>>
###Feedback Principles###

## Slide 2
We will see that feedback is a key tool that can be used to modify the behaviour of a system.
This behaviour altering effect of feedback is a key mechanism that control engineers exploit deliberately to achieve the objective of acting on a system to ensure that the desired performance specifications are achieved.
Notes: <<<2.2>>>

## Slide 3: A motivating industrial example
We first present a simplified, yet essentially authentic, example of an industrial control problem. The example, taken from the steel industry, is of a particular nature, however the principal elements of specifying a desired behaviour, modeling and the necessity for trade-off decisions are generic.
Notes: <<<2.3>>>
###Continuous Caster Control###

## Slide 4
Photograph of Bloom Caster

## Slide 5
Process schematic of an Industrial Bloom Caster

## Slide 6
Continuous caster. Typical bloom (left) and simplified diagram (right)

## Slide 7
Operators viewing the mould

## Slide 8
The cast strip in the secondary cooling chamber

## Slide 9: Performance specifications
The key performance goals for this problem are:
Safety: Clearly, the mould level must never be in danger of overflowing or emptying as either case would result in molten metal spilling with disastrous consequences.
Profitability: Aspects which contribute to this requirement include:
  Product quality
  Maintenance
  Throughput

## Slide 10: Modeling
To make progress on the control system design problem, it is first necessary to gain an understanding of how the process operates. This understanding is typically expressed in the form of a mathematical model.
commanded level of steel in mould
actual level of steel in mould
valve position
casting speed
inflow of matter into the mould
outflow of matter from the mould

## Slide 11
Model as simple tank
Tundish
Valve
Molten Steel
Mould Level
Cooling Water

## Slide 12
Block diagram of the simplified mould level dynamics, sensors and actuators
These variables are related as shown below:

## Slide 13: Feedback and Feedforward
We will find later that the core idea in control is that of inversion. Moreover, inversion can be conveniently achieved by the use of two key mechanisms (namely, feedback and feedforward).

## Slide 14
Figure 2.4: Model of the simplified mould level control with
feedforward compensation for casting speed
Note that this controller features joint feedback and a
preemptive action (feedforward).
Suggested Control Strategy:

## Slide 15: A first indication of trade-offs
On simulating the performance of the above control loop for K=1 and K=5, see Figure 2.5, we find that the smaller controller gain (K=1) results in a slower response to a change in the mould level set-point. On the other hand, the larger controller gain (K=5), results in a faster response but also increases the effects of measurement noise as seen by the less steady level control and by the significantly more aggressive valve movements.

## Slide 16
Figure 2.5: A first indication of trade-offs: Increased
responsiveness to set-point changes also increases
sensitivity to measurement noise and actuator wear.

## Slide 17: Question
We may ask if these trade-offs are unavoidable or whether we could improve on the situation by such measures as:
better modelling
more sophisticated control system design
This will be the subject of the rest of our deliberations.
(Aside: Actually the trade-off is fundamental as we shall see presently).

## Slide 18: Definition of the control problem
Abstracting from the above particular problem, we can introduce:
Definition 2.1:
The central problem in control is to find a technically feasible way to act on a given process so that the process behaves, as closely as possible, to some desired behaviour. Furthermore, this approximate behaviour should be achieved in the face of uncertainty of the process and in the presence of uncontrollable external disturbances acting on the process.
Notes: <<<2.4>>>

## Slide 19: Prototype solution to the control problem via inversion
One particularly simple, yet insightful way of thinking about control problems is via inversion. To describe this idea we argue as follows:
say that we know what effect an action at the input of a system produces at the output, and
say that we have a desired behaviour for the system output, then one simply needs to invert the relationship between input and output to determine what input action is necessary to achieve the desired output behaviour.
Notes: <<<2.5>>>

## Slide 20
Figure 2.6: Conceptual controller
The above idea is captured in the following diagram:

## Slide 21
We will actually find that the inverse solution given on the last slide holds very generally.
Thus, all controllers implicitly generate an inverse of the process, in so far that this is feasible. However, the details of controllers will differ with respect to the mechanism used to generate the required approximate inverse.

## Slide 22: High gain feedback and inversion
We next observe that there is a rather intriguing property of feedback, namely that it implicitly generates an approximate inverse of dynamic transformations, without the inversion having to be carried out explicitly.
The loop implements an approximate inverse of f , i.e. u = f r, if
r - h-1u  r
Figure 2.7:
Realisation of
conceptual controller
Notes: <<<2.6>>>
###High Gain Feedback and Inversion###

## Slide 23
Specifically,
or
Hence
Provided is small, i.e. is high gain.

## Slide 24
The above equation is satisfied if h-1u is large. We conclude that an approximate inverse is generated provided we place the model of the system in a high gain feedback loop.

## Slide 25: Example 2.3
Assume that a plant can be described by the model
and that a control law is required to ensure that y(t) follows a slowly varying reference.
One way to solve this problem is to construct an inverse for the model which is valid in the low frequency region. Using the architecture in Figure 2.7, we obtain an approximate inverse, provided that h has large gain in the low frequency region.

## Slide 26
Figure 2.8: Tank level control using approximate inversion
Simulating the resultant controller gives the results
below:

## Slide 27: From open to closed loop architectures
Unfortunately, the above methodology will not lead to a satisfactory solution to the control problem unless:
the model on which the design of the controller has been based is a very good representation of the plant,
the model and its inverse are stable, and
disturbances and initial conditions are negligible.
We are thus motivated to find an alternative solution to the problem which retains the key features but which does not suffer from the above drawbacks.
Notes: <<<2.7>>>
###Closed Loop Architecture###

## Slide 28
Figure 2.9: Open loop control with built-in inverse
Figure 2.10: Closed loop control

## Slide 29
The first thing to note is that, provided the model represents the plant exactly, and that all signals are bounded (i.e. the loop is stable), then both schemes are equivalent, regarding the relation between r(t) and y(t). The key differences are due to disturbances and different initial conditions.
In the open loop control scheme the controller incorporates feedback internally, i.e. a signal at point A is fed back.

## Slide 30
In the closed loop scheme, the feedback signal depends on what is actually happening in the plant since the true plant output is used.
We will see later that this modified architecture has many advantages including:
  insensitivity to modelling errors;
  insensitivity to disturbances in the plant (that are not reflected in the model).

## Slide 31: Trade-offs involved in choosing the feedback gain
The preliminary insights of the previous two sections would seem to imply that all that is needed to generate a controller is to put high gain feedback around the plant. This is true in so far that it goes. However, nothing in life is cost free and this also applies to the use of high gain feedback.
For example, if a plant disturbance leads to a non-zero error e(t), in Figure 2.10, then high gain feedback will result in a very large control action u(t). This may lie outside the available input range and thus invalidate the solution.
Notes: <<<2.8>>>

## Slide 32
Another potential problem with high gain feedback is that it is often accompanied by the very substantial risk of instability. Instability is characterised by self sustaining (or growing) oscillations. As an illustration, the reader will probably have witnessed the high pitch whistling sound that is heard when a loudspeaker is placed too close to a microphone. This is a manifestation of instability resulting from excessive feedback gain. Tragic manifestations of instability include aircraft crashes and the Chernobyl disaster in which a runaway condition occurred.

## Slide 33
Yet another potential disadvantage of high loop gain was hinted at in the mould level example. There we saw that increasing the controller gain lead to increased sensitivity to measurement noise. (Actually, this turns out to be generically true).

## Slide 34
In summary, high loop gain is desirable from many perspectives but it is also undesirable when viewed from other perspectives. Thus, when choosing the feedback gain one needs to make a conscious trade-off between competing issues.

## Slide 35
The previous discussion can be summarised in the following statement:
High loop gain gives approximate inversion which is the essence of control. However, in practice, the choice of feedback gain is part of a complex web of design trade-offs. Understanding and balancing these trade-offs is the essence of control system design.

## Slide 36: Measurements
Finally, we discuss the issue of measurements (i.e. what it is we use to generate the feedback signal).
A more accurate description of the feedback control loop including sensors is shown in Figure 2.11.
Notes: <<<2.9>>>
###Measurements###

## Slide 37
Figure 2.11: Closed loop control with sensors

## Slide 38: Desirable attributes of sensors
Reliability. It should operate within the necessary range.
Accuracy. For a variable with a constant value, the measurement should settle to the correct value.
Responsiveness. If the variable changes, the measurement should be able to follow the changes. Slow responding measurements can, not only affect the quality of control but can actually make the feedback loop unstable. Loop instability may arise even though the loop has been designed to be stable assuming an exact measurement of the process variable.

## Slide 39
Noise immunity. The measurement system, including the transmission path, should not be significantly affected by exogenous signals such as measurement noise.
Linearity. If the measurement system is not linear, then at least the nonlinearity should be known so that it can be compensated.
Non intrusive. The measuring device should not significantly affect the behaviour of the plant.

## Slide 40
Figure 2.12: Typical feedback loop
In summary, a typical feedback loop (including sensor
issues) is shown below.
Notes: <<<2.10>>>